## Slide 1: Basic Programming Course for T5830
CONFIDENTIAL
PRELIMINARY

## Slide 2: INDEX
Image of Tester Hardware
Introduction of T5830
Basic of programming
  How to compile
  How to write socket-file
  How to write main-program
  How to write pattern-program
Optional units
  How to use DBM
  How to use UBM
  How to use BBM
  How to use ECC
  How to use FlashCounter
  How to use FCM
  How to use Match Group
  How to use PDS memory

## Slide 3: Image of hardware
Abbreviation introduction
  ALPG ALgorithmic Pattern Generator
  DBM Data Buffer Memory
  UBM Universal Buffer Memory
  TG Timing Generator
  PDS Pin data selector
  FC Format Controller
  DR Driver
  CP Comparator
  DC Direct Current
  SC Sense Controller
  ECC Errror Correct Code function
  BBM Bad Block Memory
  FCM Fail Capture Memory
  PPS Programable Device Power Supply
  ADC Analog Digital Converter
Target
Device
DR
CP
DR
CP
IO
IO
PPS
FC
TG
SC
ALPG
BBM
FCM
ECC/FlashCounter
UBM
PDS
DBM
ADC
T5830
DC
Per Pin Unit
common
Test Site
Processor

## Slide 4: T5830 System Introduction Future Powerful & economical flash-WT/FT solution
CONFIDENTIAL
PRELIMINARY

## Slide 5
Universal, Extendable Platform for Testing Memory ICs
Blue: Roadmap
Black: Released
Digital
PPS
Infrastructure
Similar Docking Interface
FutureSuite Software
Flexible Parallelisms + Scalable PPS + Scalable Performance
Tester-per-Site, Full ATE Capability & Performance
T5831
1.2Gbps (NAND, LPDDR2)
PSM96 (96ch @ 800mA)
PSM144 (144ch @ 1200mA)
M624x 768para
T5800-ES (2-3 slots)
T5833
2.4Gbps (NAND, NVM, LPDDR3/4)
T5851
8Gbps (UFS2.x, PCIe G1-3)
Asakaze5
7Gbps (LPDDR5)
T5830
800Mbps
Inc.PPS (SPI/FP-NOR, NAND)
Ashland-2
16Gbps (PCIe G4, UFS3.0)
T5800-QSTH (64 slots)
FT & WT MBs
T5800-DSTH (44 slots)
T5800 Platform Series
HV-Level DR (288ch @ -10 to 30v)
Notes: Currently, Advantest offer several types of digital module such as T5831, T5833, T5851 and T5830
in order to meet each best fit device application needs ,
and also we have PPS dedicated modules to make it configured flexibly.
Physically those different types of module can be fit into the common variety type of
infrastructure TH from ES to Quad type of production test head.
This T5800 series make it customers deployment risk reduced and ROI improved due to the upgradable capability.

## Slide 6
NAND final test
LP DRAM final test
PC DRAM final test
[not all products shown]
NOR final test
NAND wafer sort
NOR wafer sort
T5833
1.2GHz
2.4Gbps
T5503/A
1.143 GHz/2.286 Gbps/3.2 Gbps
5KDR, 3KIO
T5503HS
2.285GHz / 4.571Gbps
1KDR, 8KIO
T5503WS
1.143 GHz/2.286 Gbps/3.2 Gbps
2.5KDR, 1.5KIO
T5830 enables a seamless transition with least risk from Advantest legacy memory solutions widely installed in WW OSATs
Ensure the lowest CoT, even the for low-pin count/severe niche flash segment
T5830
400 MHz
800Mbps
9K IO
DRAM wafer sort
T5830 product positioning
in Memory Tester Portfolio
Notes: Now, hopefully as you people know our Advantest memory tester portfolio
For each segment respectively,
Briefly, all key memory testing segments are covered with our existing memory solution like this.
For example, T5503A is more like industory market DRAM at-speed standard solution,
And T5503HS was released into higher performance segment like LP-DDR4 which is coming from now on especially
For flag ship mobile devices.
And when it comes to cost sensitive NAND application back-end while getting higher I/F like Toggle or ONFI NAND,
We released T5831 to cover such HS-NAND as well as LP-DDR2 testing .
And in the last June, we successfully made it released T5833 which is capalble of testing from LP-DDR3 to HS-NAND with
One platfrom , it is more like a super-set valuable solution combined T5503A and T5831 economically as well as post-T5385 with
Higher MRA performance to be able to cover complex DRAM –WS. Later, I will focus introducing the latest released product as T5833
Systems more in detail.
In terms of the relatively niche kind of segment for NOR flash, many our legacy memory solution are up and running in the maket.

## Slide 7: T5830 Product Overview

## Slide 8: T5830 Value Proposition
Fully Optimized, Scalable & Economical Flash Solution
T5800 series (AS-platform) module architecture to enhance ROI with less risk
Full Functionality & Flexibility for Flash Test
Provides full WT & FT test coverage for LPC-SPI NOR/NAND and Smart cards
All I/O architecture with plenty native VIHH resources for maximum flexibilty
800Mbps sufficient performance in the segment
Effective Resource Utilization
Test program compatibility: FutureSuite based
Seamless platform transition from legacy install base
Best CoT Performance
Enable Best COT performance
*Beta-site benchmark: Proved more than 20~50% TTR
& 30% CoT reduction vs. legacy V-series Flash solution in Q1, 2016
8

## Slide 9: T5830 Flexible/Scalable Configuration
9
System Configuration
Parallelism(@ 32-TOM full-config)
Speed: 800Mbps
Max. PE channels: 9216 full-IO (@TOM: Tester On Module x32 max.)
Test head type： DSTH (New, compact, lower cost infrastructure)
WMB : 32TOM (PC-480mmφWMB)
FT-MB : 32TOM
(Optional) HV-level driver module: 288 channel(@-10 to +30V: VSIM/MVM)
WT: ~ 2304 DUT parallelism @ 4 digital pin * Industry Leading
~ 1536 DUT parallelism @ 6 digital pin
Target Applications
NOR/NAND/NVM(LPC SPI, FPC), other embedded Flash as MCU

## Slide 10: Exceptional Turn-Key Test solution
Advantest Handlers
M624x, Optimal Test Handler with Double the Throughput
Proven for Mass-Production
512 parallelism
Advantest DI for final test
Cable-Connected HIFIX
SBC-Type HIFIX (Socket Board Change)
IC Sockets, Change Kit
Advantest DI for wafer test
Wafer HIFIX, support wafer probers from a variety of companies
BIST batch probe card offers high throughput and low costs for Flash
WMB
Probe Card
M624x
SBC-Type HIFIX
Ensures product quality assurance with leading edge one-stop support

## Slide 11: TOM (Tester On Module) Block Diagram
PIN
CONT
LKIF
TSC
(2 core)
TOM
TOTAL
288 I/O ch
72 PPS ch
per Module
PPS
CONT
144 I/O ch
36 PPS ch
FuncBlock A
Site1
36 PPS
DRCP(2ch) x 24
48 I/O
ADC
FUNC
DC1
DC2
DC3
DC4
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
FuncBlock B
48 I/O
ADC
FUNC
DC1
DC2
DC3
DC4
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
FuncBlock C
48 I/O
ADC
FUNC
DC1
DC2
DC3
DC4
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
DRCP(2ch) x 24
DRCP(2ch) x 24
to Func
to DCL
to PPS
to DC
12PPS x 3branch
PPS7
1200mA
PPS1
1200mA
PPS8
1200mA
PPS2
1200mA
PPS9
1200mA
PPS3
1200mA
PPS10
1200mA
PPS4
1200mA
PPS11
1200mA
PPS5
1200mA
PPS12
1200mA
PPS6
1200mA
PIN
CONT
PPS
CONT
FuncBlock A
Site2
36 PPS
DRCP(2ch) x 24
48 I/O
ADC
FUNC
DC1
DC2
DC3
DC4
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
FuncBlock B
48 I/O
ADC
FUNC
DC1
DC2
DC3
DC4
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
FuncBlock C
48 I/O
ADC
FUNC
DC1
DC2
DC3
DC4
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
VHH
DRCP(2ch) x 24
DRCP(2ch) x 24
to Func
to DCL
to PPS
to DC
12PPS x 3branch
PPS7
1200mA
PPS1
1200mA
PPS8
1200mA
PPS2
1200mA
PPS9
1200mA
PPS3
1200mA
PPS10
1200mA
PPS4
1200mA
PPS11
1200mA
PPS5
1200mA
PPS12
1200mA
PPS6
1200mA
Site 1
144 I/O ch
36 PPS ch
Site 2
(Site1)
(Site2)

## Slide 12
Quadrant B |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22
22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Quadrant A |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
DSTH Test Head type
WMB | TOM | NEW MODULE | IO | PPS | HV LVL
Type A | 12 | 6 | 3,456 | 864 (400mA) | 1,728
 | 16 | 6 | 4,608 | 1,152 (400mA) | 1,728
 | 18 | 6 | 5,184 | 1,296 (400mA) | 1,728
Type B | 16 | - | 4,608 | 1,152 (400mA) | -
 | 32 | - | 9,216 | 2,304 (400mA) | -
480mmφ
For SPI NOR(NAND), Full 32 TOM with type B WMB configuration
ensure the best CoT performance in WW
T5830 System Configuration

## Slide 13: T5830 Specification

## Slide 14: System Specification (ES)
ITEM |  | T5830ES | T5000e
Max. Frequency |  | 400MHz/800Mbps | 50MHz/100Mbps
Accuracy | OTA | +/-350ps (Target) | +/-1ns
 | Dr/Cp Skew | 200ps p-p (Target) | 156ps p-p
TH Channels | IO | 288 | 128
 | DR | - | -
 | LVLDR | - | -
 | PPS | 24 x 3 port= 72@400mA | VCC: 4 x 2 port=8@400mA VPP: 4@400mA VNN: 4@400mA
HV-LVLDR(Optional) |  | 32 | -
Load | Passive Load | 72( 1 per 4 I/O pins) | 128( per pin)
 | Programmable Load | - | -
DC |  | 24 | 4
Formatter Channels |  | 48IO | 128IO

## Slide 15: TG/FC
ITEM |  | T5830 | T5000e
Rate Setting Range |  | 2.5ns to 10us | 20ns to 102.4us
Clock Setting Range |  | 0ns to 2us ( Max <= Rate ) | -
Rate Resolution |  | (Base Period / 8) | 1ns
Timing Edge |  | BCLK, CCLK, DREL, DRET, STRB1-2 | IO1,2, DRST, DREN, STRST, STREN
Timing Set |  | 16 | 14
Formatter Channels |  | 48IO | 128IO
Wave Form | DR | NRZ, RZ, XOR, FIX, DNRZ | SBC, SBO, RTO, RTZ, RIO,NR CN,CL,CZ,NC
 | DRE | NRZ | 
Cycle Palette |  | 16 | 64
Serializer |  | 128 words x 4sets | (ACAM/ECAM)

## Slide 16: ALPG (1/2)
ITEM | T5830 | T5000e
Interleave | 2WAY | 1WAY
WCS | 4K words | 4K words
X/Y/Z address | 24bits / 24bits / 24bits | 16bits / 16bits / 16bits
TP1 / TP2 | 36bits / 36bits | 32bits / 32bits
MUT Signal | R, W, M1, M2, C0-31 | (DUT jamming/ECR2/3)
DBM (Access by DBMAP or X/Y) | 64M words x 48bits 128M words x 24bits 256M words x 12bits 512M words x 6bits 1G words x 3bits 2G words x 1bit Load the data of up to 32K words(@ w/o UBM use) | 8Mbit x 4 (pattern memory)
UBM (Access by UBMAP) | 16k words per IO Only individual pattern generation | -
Scrambler | - | YES

## Slide 17: ALPG (2/2)
ITEM | T5830 | T5000e
DFM | 1K words | -
BBM (BadBlockMemory) | (36K words x 12DUT) per 48IO (72K words x 8DUT) per 48IO (144K words x 4DUT) per 48IO | ECR2: 32 Kb ECR3: 128 Kb
BBC (BadBlockCounter) | (21bits x 12sets) per 48IO | – One 17-bit Column Counter and its 16-data bit mask – One 14-bit Row Counter and its 16 to 1 compression
Flash Counter | (32bits x 12sets) per 48IO | 
AFM | (128M words x 32bits) per 48IO (128M words x 24bits) per 48IO (*1) Save data of up to 32K words each (*1) at using HW scan for RA | 256 Mb @ 50 MHz 512 Mb @ 25 MHz 768 Mb @ 50/3 MHz 1536 Mb @ 50/6 MHz
PFC (Parallel Fail Counter) | (31bits x 32sets) per 48IO Fail in duplicate addresses is counted | – 16 sets of 16-bit General Purpose Post-Decode counters and their – One 32-bit Address Accumulator – One 32-bit Bitwise Accumulator counter
RTCM (Real Time Counter Memory) | - | 
CFM (Compact Fail Memory) | 1Mbits per 48IO | ECR2: 32 Kb ECR3: 128 Kb

## Slide 18: PE
ITEM |  | T5830 | T5000e
Driver | Output Voltage | VIH : -0.5V to 6.00V VIL : -1.0V to 5.65V | VIH : -0.25 to +6.5 V VIL : -0.5 to +6.25 V
 | Amplitude | 0.35V to 6.75V | Vil 1 and 2 – Vih 1 and 2 must be < 5 V
 | Current | ±30mA | ?
 | Rise/Fall Time | 400ps@1Vp-p(20%-80%) | ?
 | Min. PW | 1.25ns@1V | ?
High Voltage Driver | Output Voltage | VHH : 0V to 13V | VIHH : 0 to +13 V
 | Current | ± 2.5mA (VHH ≦ 13V) ±10.0mA (VHH ≦ 12V) | ±10.0mA
 | Impedance | 100 ohm (max) | ?
Comparator | Input Level | Single Level (Edge) | Dual Level
 | Input/Ref. Voltage | -1.0V to 6.0V (single comparator: VOH only) | -0.5 to +6.5 V
Terminator | Termination Voltage | VTT : -1.0V to 5.75V | VTT : -0.5 to +6.5 V
 | Current | ±30mA | ±35mA
 | Impedance | 50 ± 5 ohm | ?
Passive Load |  | 0.5k ohm (±14mA max) 1.0k ohm (±7mA max) 8.0k ohm (±1mA max) | N/A(VCOM-0.5 to +6.5 V)

## Slide 19: DC
ITEM |  | T5830 | T5000e
VSIM | Voltage Setting | -1.0V to +13.0V | Through PPS, -22 to +22 V Through PE, -1.5 to +13.0 V
 | Current Measurement | ±10mA (-1.0V to 0.0V) ±20mA ( 0.0V to + 9.0V) ±5.0mA (+9.0V to +12.5V) ±2.5mA (+12.5V to +13.0V) | ±2.5μA; ±25μA; ±250μA ±2.5mA; ±25mA; ±50mA;
ISVM | Current Setting | 0A to ±20mA | 0A to ±128mA
 | Voltage Measurement | -1.0V to 0.0V (0A to ±10mA) 0.0V to +9.0V (0A to ±20mA) +9.0V to +12.5V(0A to ±5.0mA) +12.5V to +13.0V(0A to ±2.5mA) | Through PPS, -22 to +22 V Through PE, -1.5 to +13.0 V
MVM | Voltage Measurement | - | DVM mode

## Slide 20: PPS
ITEM | T5830 | T5000e
Voltage Setting | -1.0V to +13.0V | VCC: 0 to 12 V VPP:0 to 13 V VNN:–10 to +5 V
Maximum Current | 1.2A @ 3.3V (3-Branch total) 1.0A @ 4.0V (3-Branch total) 400mA @ 13.0V (3-Branch total) | VCC: 800mA VPP:400mA VNN:400mA
Current Measurement | YES | YES

## Slide 21: EWS, TP, RCPU, Software
ITEM | T5830 | T5000e
Work Station | Intel Xeon 2.66GHz | Windows XP
Test Processor | ARM 1.2GHz 2core x N （See. Note) | Power PC 400Mhz?
System Software | FutureSuite (ATL compatible) | VK システムソフトウェア
RCPU (Option) | Intel Xeon architecture | -
MRA Software (Option) | FutureSuite MRA ( MRA4,Universal MRA compatible) | -
(Note)
TOM x 16 → N=16
TOM x 32 → N=32

## Slide 22: Utility
ITEM | T5830 | T5000e
PBVCC | P5VPB : 5.0V ± 5% P5VPBRL : 5.0V ± 5% ( P3R3VPB : 3.3V ± 5% ) | (Refer to V5000 utility information)
PBVCC Total Current | P5VPB : 15A P5VPBRL : 15A ( P3R3VPB : 4A ) | (Refer to V5000 utility information)
Control Function | LBCNT | LBIO

## Slide 23
ITEM |  | HV LVL DR
Channel |  | 48ch PPS x 6 branch = 288 output ch/ module
VSIM | Output Voltage | -10V ～ +30V
 | VS Resolution | 4mV
 | Current Measurement | -80mA ～ +90mA (per Unit)
 | IM Resolution | 40uA
 | Max. Capacitive load | 0.1 uF (per each of 288 output ch)
MVM | Voltage Measurement | -10V ～ +30V
 | VM Resolution | 4mV
T5830 HV LVL DR module (option)

## Slide 24: T5800 Series High Voltage Level Drier Module
CONFIDENTIAL

## Slide 25: HV-LVL DR Module- Block Diagram
15mA
Probe Card side (example)
VSIM mode
12 output channel / MC * 24 MC = 288 output channel / module
Unit 1
90mA
Unit 2
90mA
1 MC = 2Unit x 6 brunch
Unit 3
90mA
Unit 4
90mA
Unit 47
90mA
Unit 48
90mA
MC #1
MC #2
MC #24
CONT
MVM mode
M I/F
HV LVL DR module
Each “MC” block can be selected “VSIM” or “MVM”
mode independently.
15mA

## Slide 26: HV-LVL DR Module- Specification
Channel |  | 48ch VPP x 6 branch = 288 output ch/ module |  |  | 
Setting Range |  | Output Voltage | Resolution | Max. Current | Accuracy
VSIM | 8V | -8V to +8V | 1mV | -80mA～90mA | ±(0.1%+4mV+7.0mV/10mA)
 | 32V | -10V to +32V | 2mV | -80mA~90mA | ±(0.2%+16mV+7.0mV/10mA)
Current Range |  | Measurement Range | Resolution | Measurement Accuracy | 
VSIM | 8uA | -8uA to +8uA | 0.25nA | ±(0.5%+56nA+0.5nA/V) | 
 | 80uA | -80uA to +80uA | 2.5nA | ±(0.2%+90nA+5nA/V) | 
 | 800uA | -800uA to +800uA | 25nA | ±(0.2%+450nA+50nA/V) | 
 | 8mA | -8mA to +8mA | 0.25uA | ±(0.2%+4.05uA+0.5uA/V) | 
 | 128mA | -80mA to +90mA | 5uA | ±(0.5%+120uA+10uA/V) | 
Voltage Range |  | Measurement Range | Resolution | Measurement Accuracy | Input Impedance
MVM | +8V | -0.3V to +8V | 1mV | ±(0.1%+4mV) | 10MΩ<
 | -8V | -8V to +0.3V | 1mV | ±(0.1%+4mV) | 10MΩ<
 | +32V | -0.3V to +32V | 4mV | ±(0.2%+16mV) | 10MΩ<
 | -32V | -10V to +0.3V | 4mV | ±(0.2%+16mV) | 10MΩ<

## Slide 27: T5830ES Floor Plan
Secure space for maintenance approximately 1 m between the rear surface of the mainframe and the wall.
The height of the room from floor to ceiling must be at least 2.4 m.
The outer dimensions (height x width x depth) of the mainframe and test head are as follows:
• MF: 1650 mm x 850 mm x 1050 mm
• TH: 640 mm x 830 mm x 1490 mm
• Monitor desk (option): 680 mm x 650 mm x 900 mm

## Slide 28: T5830 Floor Plan (DSTH)

## Slide 29: Basic of programming

## Slide 30: File Component
main program
    C program. To access tester hardware, call MCI functions.
    C程序。若要访问测试仪硬件，请调用MCI函数
socket file
    The table of combination between DUT and PIN number
    DUT与PIN数 组合表
pattern program
    Assembler program of ALPG
    ALPG汇编

## Slide 31: How to compile

## Slide 32: To compile main program
Compiler
      For ONLINE : arm-marvell-linux-gnueabi-gcc/arm-marvell-linux-gnueabi-g++
      For TESIM : gcc/g++
Preprocessor Options
      -I/opt/ATFS/arm/linux/${ATFSSYS}/include \
      -I/opt/ATFS/arm/linux/${ATFSDIAG}/include \
      -I/opt/ATFS/arm/linux/${ATFSTBUS}/include \
      -I/opt/ATFS/arm/linux/${ATFSATL}/include \
      -I/opt/ATFS/arm/linux/${ATFSVTC}/include
Compile Options
      -Wall -O -fPIC
Link Options
      -L/opt/ATFS/arm/linux/${ATFSSYS}/lib \
      -L/opt/ATFS/arm/linux/${ATFSDIAG}/${ATFSTMODEL}/lib \
      -L/opt/ATFS/arm/linux/${ATFSTBUS}/lib \
      -L/opt/ATFS/arm/linux/${ATFSVTC}/${ATFSTMODEL}/lib \
      -latfssock -latfsmcicl -latfsvtc -latfstb -latfsrc -latfssc -latfshn -lnsl -lrt -ldl -lresolv -lm
It’s too long to remember and
difficult to
input correctly

## Slide 33: Makefile
Because compiler options are too long to remember and difficult to input correctly, make is recommended to compile your code correctly.
EXE = pro_nandflash.exe
PAT = pat_nandflash.mpa
OBJ = pro_nandflash.o
CC = gcc
LD = gcc
CPPFLAGS = -I${ATFSSYSTEM}/${ATFSATL}/include \
-I${ATFSSYSTEM}/${ATFSSYS}/include \
-I${ATFSSYSTEM}/${ATFSVTC}/include \
-I${ATFSSYSTEM}/${ATFSTBUS}/include
CFLAGS = -Wall -O -fpic
LDFLAGS = -L${ATFSSYSTEM}/${ATFSDIAG}/lib \
-L${ATFSSYSTEM}/${ATFSATL}/lib \
-L${ATFSSYSTEM}/${ATFSSYS}/lib \
-L${ATFSSYSTEM}/${ATFSTBUS}/lib \
-L${ATFSSYSTEM}/${ATFSSYS}/${ATFSTMODEL}/lib \
-L${ATFSSYSTEM}/${ATFSSYS}/${ATFSBMODEL}/lib \
-L${ATFSSYSTEM}/${ATFSVTC}/${ATFSTMODEL}/lib \
-L${ATFSSYSTEM}/${ATFSDIAG}/${ATFSTMODEL}/lib
LDLIBS = -latfssock -latfsmcicl -latfsvtc -latfstb -latfsrc -latfssc -latfshn \
-lnsl -lrt -ldl -lresolv -lm
DFILES = ${OBJ:.o=.d} ${PAT:.mpa=.d}
ALL: ${EXE} ${PAT}
clean:
${RM} *.pro *.mpa *.o *.d
%.exe:%.o
${LD} $< -o $@ ${LDFLAGS} ${LDLIBS}
%.d:%.c
@${CC} ${ATFS_INCS} -MM $< > $@
%.mpa: %.asc
trans ${TRANSOPT} $<
-include ${DFILES}
It is enough to add object file name list here
The Object file name is same name of Source File except extension.
(Source:***.c -> Object: ***.o)

## Slide 34: To compile with Makefile
Run ‘make’ command to compile all files.
% make
When you copies whole directly to new environment, you should remove temporary files of compile. At that time, ‘make clean’ will help you to remove all unnecessary files
% make clean

## Slide 35: To compile pattern program
‘trans’ command is used to compile pattern programs.
% trans pat_nandflash.asc
Off course, pattern program also can be compiled with ‘make’ command.

## Slide 36: How to write Socket file

## Slide 37: Outline
Socket file is written the relationship of tester pin resource for each DUT.
Pin | DUT1 | DUT2 | DUT3 | DUT4 | DUT5 | DUT6 | DUT7 | DUT8
VCC | PPS4A | PPS1A | PPS2A | PPS3A | PPS8B | PPS5B | PPS6B | PPS7B
CE_n | PD044A | PD049A | PD044C | PD049C | PD044B | PD010A | PD010B | PD010C
CLE | PD056A | PD033A | PD056C | PD033C | PD033B | PD009A | PD009B | PD009C
ALE | PD055A | PD034A | PD055C | PD034C | PD034B | PD007A | PD007B | PD007C
WE_n | PD054A | PD036A | PD054C | PD036C | PD036B | PD006A | PD006B | PD006C
RE_n | PD041A | PD050A | PD041C | PD050C | PD041B | PD012A | PD012B | PD012C
WP_n | PD053A | PD035A | PD053C | PD035C | PD035B | PD005A | PD005B | PD005C
DQ0 | P037A | P017A | P037C | P017C | P037B | P001A | P001B | P001C
DQ1 | P038A | P019A | P038C | P019C | P038B | P002A | P002B | P002C
DQ2 | P040A | P021A | P040C | P021C | P040B | P003A | P003B | P003C
DQ3 | P039A | P023A | P039C | P023C | P039B | P004A | P004B | P004C
DQ4 | P046A | P024A | P046C | P024C | P046B | P013A | P013B | P013C
DQ5 | P045A | P022A | P045C | P022C | P045B | P014A | P014B | P014C
DQ6 | P048A | P020A | P048C | P020C | P048B | P015A | P015B | P015C
DQ7 | P047A | P018A | P047C | P018C | P047B | P016A | P016B | P016C
RB_n | P043A | P051A | P043C | P051C | P043B | P011A | P011B | P011C

## Slide 38: Sample Socket File
Write one DUT pin resource information in a line. DUT# is Represent number. The setting of PD1 in main program is copied to PD44A, PD49A, PD44C, PD49C, PD10A, PD10B and PD10C. The extension of socket-file must be “.soc”
SOCKET soc_nandflash
DEFINE MULTIPLE 8DUT 1STN 2SITE
BIT = 9
PPS = 1
; VCC CE CLE ALE WE RE WP DQ0 DQ1 DQ2 DQ3 DQ4 DQ5 DQ6 DQ7 RB
DUT# = VS1 PD001 PD002 PD003 PD004 PD005 PD006 P033 P034 P035 P036 P037 P038 P039 P040 P041
DUT1 = PPS4A PD044A PD056A PD055A PD054A PD041A PD053A P037A P038A P040A P039A P046A P045A P048A P047A P043A
DUT2 = PPS1A PD049A PD033A PD034A PD036A PD050A PD035A P017A P019A P021A P023A P024A P022A P020A P018A P051A
DUT3 = PPS2A PD044C PD056C PD055C PD054C PD041C PD053C P037C P038C P040C P039C P046C P045C P048C P047C P043C
DUT4 = PPS3A PD049C PD033C PD034C PD036C PD050C PD035C P017C P019C P021C P023C P024C P022C P020C P018C P051C
DUT5 = PPS8B PD044B PD033B PD034B PD036B PD041B PD035B P037B P038B P040B P039B P046B P045B P048B P047B P043B
DUT6 = PPS5B PD010A PD009A PD007A PD006A PD012A PD005A P001A P002A P003A P004A P013A P014A P015A P016A P011A
DUT7 = PPS6B PD010B PD009B PD007B PD006B PD012B PD005B P001B P002B P003B P004B P013B P014B P015B P016B P011B
DUT8 = PPS7B PD010C PD009C PD007C PD006C PD012C PD005C P001C P002C P003C P004C P013C P014C P015C P016C P011C
END

## Slide 39: How to write Main Program
Device organization for Single-Die Package

## Slide 40: Main Program
MCI program start from main() or test_main()
  int main( int argc, char **argv);
  int test_main ();
      W/ main() function, the program start from main().
      W/O main() function, the program start from test_main().
      W/O main, w/o test_main(), RTE happens when started.

## Slide 41: MCI basic
Evey setting is based on "Handle". Handle is a kind of pointer to point a memory area to save data.
For example, For Driver Input Voltage setting, ViHandle is used. ViHandle points a memory area to save High Voltage and Low Voltage of Driver.
Basic Sequence is Get Handle, Setting each values and Send the Handle data into hardware.
When the handle is not necessary, you can release the memory area for that handle by using UTL_DeleteHandle().
ViHandle
VIH
VIL
ViHandle vi_handle_dq = UTL_GetViHandle();
UTL_SetViHigh( vi_handle_dq, 3.30 V);
UTL_SetViLow ( vi_handle_dq, 0.00 V);
UTL_SendVi ( vi_handle_dq, IN 1 );

## Slide 42: PINLIST
Tester pin resources and device pins require mapping in order to be used in the test program.
First, a Pinlist Name for each kind of assignment must be created. You may have Pinlist Names such as "DQ", or "WE_n", etc. Pins that normally work together as a group can be part of a Pinlist Name, or even individual pins if they are normally used alone.
Next, for each Pinlist Name, a Pinlist Table is created to map Tester Pin Resources to Device Pins.
Finally, this is all assembled into a Pinlist Function which makes these Pinlist assignments available to the test program.
UTL_CreatePinList("WE_n" );
UTL_SetPinType ("WE_n", UT_PINTYPE_PIN);
UTL_AddPinNumber ("WE_n", 4 );

## Slide 43: Pin/Timing/Level Setting
Use this common setting of Pin/Timing/Level for all Function Test.
TS1
TS1
TS1
TS1
TS1
TS2
TS1
0ns
60ns
RATE<1>=100ns
RATE<2>=1us
RB
VL2=3.3V
CS_n
0ns
/NRZB
VIH=3.3V
VIL=0.0V
WE_n
10ns
70ns
/RZO
VIH=3.3V
VIL=0.0V
RE_n
/RZO
VIH=3.3V
VIL=0.0V
WP_n
FIXH
VIH=3.3V
VIL=0.0V
ALE
0ns
NRZB
VIH=3.3V
VIL=0.0V
CLE
NRZB
VIH=3.3V
VIL=0.0V
DQn
0ns
NRZB
VIH=3.3V
VIL=0.0V
Hi-Z
VOH=1.70V
CMD
DIN
DATA
0ns
ADDR
VOH=1.650V
Tester Output
Device Output
STRB=60ns
STRB=0ns

## Slide 44: Hardware outline
Each pin has PDS and format control unit. ALPG generate a pattern for each MUT and PDS for each pin selects necessary MUT and make waveform by Format Control Unit with Timing
TG
ALPG
A0
WE
CE
SC
PDS
10ns
35ns
45ns
Format Control
CH1
CH2
CH3
Cycle Palette Selection
TS
DRE
CPE

## Slide 45: Waveform example with MPAT
Pattern is ‘0’/ ‘1’ data generated by ALPG and depends on PDS, WAVEFORM and timing setting, the tester driver output the signal.
BCLK
CCLK
NRZB
INRZB
RZO
IRZO
RZX
IRZX
pattern
1
1
0
0
0
START #100
NOP TS1 CYP1
NOP TS1 CYP1 C2
NOP TS1 CYP1 C2
NOP TS1 CYP1
NOP TS1 CYP1
STPS

## Slide 46: Pin Setting ~ DR ~
DR setting
  To set up Driver, it is necessary to set up Input Voltage(IN), Input Timing (BCLK, CCLK) and Waveform. To set up pins, need to use Unit-Number. For example, set Driver setting as following.
PINLIST | Waveform | Input Voltage Unit | Input Timing Unit
CE_n | /NRZB | IN1 | BCLK1
CLE | NRZB | IN2 | BCLK2
ALE | NRZB | IN3 | BCLK3
WE_n | /RZO | IN4 | BCLK4, CCLK4
RE_n | /RZO | IN5 | BCLK5, CCLK5
WP_n | FIXH | IN6 | -
DQ | NRZB | IN7 | BCLK7, CCLK7
RB | - | - | -

## Slide 47: Pin Setting example ~ DR ~
Case of WE_n, the program will be below
PinHandle pin_handle_we = UTL_GetPinHandle();
UTL_SetPinDrWaveform( pin_handle_we, UT_WAV_IRZO );
UTL_SetPinViNumber ( pin_handle_we, IN 4 );
UTL_SetPinDrClock ( pin_handle_we, UT_PIN_BCLK, BCLK 4);
UTL_SetPinDrClock ( pin_handle_we, UT_PIN_CCLK, CCLK 4);
UTL_SendPin ( pin_handle_we, "WE_n" );
PINLIST | Waveform | Input Voltage Unit | Input Timing Unit
WE_n | /RZO | IN4 | BCLK4, CCLK4

## Slide 48: Pin Setting ~ CP ~
CP setting
  To set up Comparator, it is necessary to set up Device Output Reference Voltage(OUT), Reference Timing(STRB), CPE control and expected data. To set up pins, need to use Unit-Number.
PinHandle pin_handle_dq0 = UTL_GetPinHandle();
:
UTL_SetPinVoNumber ( pin_handle_dq0, OUT 1 );
UTL_AddPinStrbCpeNumber( pin_handle_dq0, STRB 1, CPE 1 );
UTL_AddPinExpStrbNumber( pin_handle_dq0, STRB 1, UT_PIN_EXP_A);
:
UTL_SendPin ( pin_handle_dq0, "DQ0" );

## Slide 49: Pin Setting ~ IO ~
IO setting
  It is necessary to set up IO switching when the pin were bi-direction pin such as DRE(Driver Enable signal), DRECLK(DRE timing) or DRE waveform.
PinHandle pin_handle_dq0 = UTL_GetPinHandle();
:
UTL_SetPinIoCtrl ( pin_handel_dq0, UT_ON );
UTL_SetPinDreNumber ( pin_handel_dq0, DRE 1 );
UTL_SetPinDreWaveform ( pin_handle_dq0, UT_DREWAV_NRZ );
UTL_SetPinDreClock ( pin_handle_dq0, DRECLK 1 );
:
UTL_SendPin ( pin_handle_dq0, "DQ0" );

## Slide 50: Pin Setting ~ Termination ~
Termination setting
  It is necessary to set up Termination setting such as 50Ω termination=ON/OFF, IL/V-Load =ON/OFF or Termination Voltage Unit.
PinHandle pin_handle_dq0 = UTL_GetPinHandle();
:
UTL_SetPinTerm ( pin_handle_dq0, UT_OFF );
:
UTL_SendPin ( pin_handle_dq0, "DQ0" );
PinHandle pin_handle_dq0 = UTL_GetPinHandle();
:
UTL_SetPinTerm ( pin_handle_dq0, UT_ON );
UTL_SetPinVtNumber ( pin_handle_dq0, VT 1 );
:
UTL_SendPin ( pin_handle_dq0, "DQ0" );

## Slide 51: Pin Setting ~ Match Polling ~
Match polling
Because the execution time of Erase, Program or Read operation has unevenness for each device, tester have to wait until RB goes high for each device. By using MATCH function to minimamize match-polling time.
PinHandle pin_handle_rb = UTL_GetPinHandle();
:
UTL_SetPinMatchMode ( pin_handle_rb, UT_SIG_MATCH );
UTL_SendPin ( pin_handle_rb, "RB" );
DUT1’s RB
ADDR
CMD
CMD
ADDR
ADDR
R3
60h
D0h
R1
R2
DUT2’s RB
DUT3’s RB
DUT4’s RB
Command
Input
Goes next

## Slide 52: Pin Setting ~VLOAD~
VLOAD
Vload provides pull up or pull down voltage and resister such as might be needed for a Ready/Busy pin. This Ready/Busy pin has an open drain with no means to go high on its own.
VT(50Ω termination) also provide voltage and resister but because of the power consumption of Ready/Busy pin, sometimes Ready/Busy pin cannot pull it down enough agaist 50Ω resister.
PinHandle pin_handle_rb = UTL_GetPinHandle();
:
UTL_SetPinVloadNumber ( pin_handle_rb, VLOAD 2 );
UTL_SetPinVloadResistor( pin_handle_rb, UT_PIN_VLOAD_1K);
:
UTL_SendPin ( pin_handle_rb, "RB" );

## Slide 53: Pin Setting ~PDS~
The PDS provides selectable routing from ALPG pin data to the intended PE channels. The various signals generated by the ALPG are assigned to the data lines PdsDataA and PdsDataB of the PDS. The signals assigned can be used as driver pattern or as expect data.
TG
ALPG
A0
WE
CE
SC
PDS
10ns
35ns
45ns
Format Control
CH1
CH2
CH3
Cycle Palette Selection
TS
CH1
DRE/CPE
D0
ALPG generate
X0-X23, Y0-Y23
D0-D17, SD0-SD17
C0-C31, M1,M2,R,W

## Slide 54: Cycle Type Definition
4 Cycle Type are define such as CMD, ADDR, DIN and DOUT
ADDR
CMD
DIN
DOUT
0ns
60ns
RATE<1>=100ns
RATE<2>=1us
RB
VL2=3.3V
CS_n
0ns
/NRZB
VIH=3.3V
VIL=0.0V
WE_n
10ns
70ns
/RZO
VIH=3.3V
VIL=0.0V
RE_n
/RZO
VIH=3.3V
VIL=0.0V
WP_n
FIXH
VIH=3.3V
VIL=0.0V
ALE
0ns
NRZB
VIH=3.3V
VIL=0.0V
CLE
NRZB
VIH=3.3V
VIL=0.0V
DQn
0ns
NRZB
VIH=3.3V
VIL=0.0V
Hi-Z
VOH=1.70V
CMD
DIN
DATA
0ns
ADDR
VOH=1.650V
Tester Output
Device Output
STRB=60ns
STRB=0ns
 | CE_n | CLE | ALE | WE_n | RE_n
CMD | Low | High | Low | Toggle | High
ADDR | Low | Low | High | Toggle | High
DIN | Low | Low | Low | Toggle | High
DOUT | Low | Low | Low | High | Toggle

## Slide 55: Cycle palette for each use-case
NAND FLASH memory uses Time Division Multiplexing to input Command/Address/Data via DQn. To input Command/Address/Data by using Cycle Palette for each Cycle Type.
Timing Chart of Read Operation
Timing Chart of Page Program
Timing Chart of Block Erase
CYP1
CYP6
CYP2
CYP3
CYP4
CYP5
CYP6
CYP1
CYP6
CYP2
CYP3
CYP4
CYP5
CYP6
CYP6
CYP6
CYP3
CYP6
CYP4
CYP5
CYP6

## Slide 56: Cycle palette setting for ICC1 & Function Test
Setting of cycle palette depends on the previsou page use-cases.
CYP | Purpose | DQ7 | DQ6 | DQ5 | DQ4 | DQ3 | DQ2 | DQ1 | DQ0
CYP1 | Address Input(C1) | Y7 | Y6 | Y5 | Y4 | Y3 | Y2 | Y1 | Y0
 |  | Column Address(0-8639) |  |  |  |  |  |  | 
CYP2 | Address Input(C2) | FL | FL | Y13 | Y12 | Y11 | Y10 | Y9 | Y8
 |  | - | - |  |  |  |  |  | 
CYP3 | Address Input(R1) | X7 | X6 | X5 | X4 | X3 | X2 | X1 | X0
 |  |  | Page Address(0-127) |  |  |  |  |  | 
CYP4 | Address Input(R2) | X15 | X14 | X13 | X12 | X11 | X19 | X8 | X7
 |  | Block Address(0-2047) |  |  |  |  |  |  | 
CYP5 | Address Input(R3) | FL | FL | FL | FL | FL | X18 | X17 | X16
 |  | - | - | - | - | LUN=0 | Plane |  | 
CYP6 | Command & Data Input Expected for output data | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
 |  | COMMAND / DATA |  |  |  |  |  |  | 

## Slide 57: Pin Setting ~ PDS ~
PDS setting
PinHandle pin_handle_dq0 = UTL_GetPinHandle();
:
UTL_AddPinPdsA ( pin_handle_dq0, UT_SIG_Y( 0), CYP 1);
UTL_AddPinPdsA ( pin_handle_dq0, UT_SIG_Y( 8), CYP 2);
UTL_AddPinPdsA ( pin_handle_dq0, UT_SIG_X( 0), CYP 3);
UTL_AddPinPdsA ( pin_handle_dq0, UT_SIG_X( 7), CYP 4);
UTL_AddPinPdsA ( pin_handle_dq0, UT_SIG_X(16), CYP 5);
UTL_AddPinPdsA ( pin_handle_dq0, UT_SIG_D( 0), CYP 6);
:
UTL_SendPin ( pin_handle_dq0, "DQ0" );
CYP | DQ7 | DQ6 | DQ5 | DQ4 | DQ3 | DQ2 | DQ1 | DQ0
CYP1 | Y7 | Y6 | Y5 | Y4 | Y3 | Y2 | Y1 | Y0
CYP2 | FL | FL | Y13 | Y12 | Y11 | Y10 | Y9 | Y8
CYP3 | X7 | X6 | X5 | X4 | X3 | X2 | X1 | X0
CYP4 | X15 | X14 | X13 | X12 | X11 | X19 | X8 | X7
CYP5 | FL | FL | FL | FL | FL | X18 | X17 | X16
CYP6 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0

## Slide 58: Timing Setting
Use TgHandle for Timing setting.
ADDR
CMD
DIN
DOUT
RATE<1>=100ns
RATE<2>=1us
RB
DQn
BCLK7, DRECLK1
STRB1
CMD
DIN
DATA
ADDR
0ns
STRB=60ns
STRB=0ns
STRB2
TgHandle tg_handle = UTL_GetTgHandle();
#define nS *1.0e-9
#define uS *1.0e-6
UTL_AddTgRate ( tg_handle, TS 1, 100.0 nS);
UTL_AddBclk ( tg_handle, TS 1, BCLK 7, 0.0 nS); // for DQ
UTL_AddTgDreL ( tg_handle, TS 1, DREL 1, 0.0 nS); // for DQ
UTL_AddTgDreT ( tg_handle, TS 1, DRET 1, 0.0 nS); // for DQ
UTL_AddTgStrb ( tg_handle, TS 1, STRB 1, 60.0 nS); // for DQ
UTL_AddTgStrb ( tg_handle, TS 1, STRB 2, 0.0 nS); // for RB
UTL_AddTgRate ( tg_handle, TS 2, 1.0 uS);
UTL_AddBclkOff ( tg_handle, TS 2, BCLK 7 ); // for DQ
UTL_AddTgDreLOff( tg_handle, TS 2, DREL 1 ); // for DQ
UTL_AddTgDreTOff( tg_handle, TS 2, DRET 1 ); // for DQ
UTL_AddTgStrb ( tg_handle, TS 2, STRB 1, 0.0 nS); // for DQ
UTL_AddTgStrb ( tg_handle, TS 2, STRB 2, 0.0 nS); // for RB
UTL_SendTg ( tg_handle );
DRE=on
@BCLK
DRE=off
@BCLK
DREL : TIming of DRE=on
Usually always equal to BCLK
DRET : TIming of DRE=off
Usually always equal to BCLK
No Driver edge in TS2

## Slide 59: Level Setting
By using ViHandle, VoHandle, VtHandle, VloadHandle, Each Level Unit can be set up.
VloadHandle vload_handle2 = UTL_GetVloadHandle();
UTL_SetVload ( vload_handle2, 3.300 V);
UTL_SendVload ( vload_handle2, VLOAD 2);
ViHandle vi_handle7 = UTL_GetViHandle();
UTL_SetViHigh( vi_handle7, 3.300 V);
UTL_SetViLow ( vi_handle7, 0.000 V);
UTL_SendVi ( vi_handle7, IN 7 );
VoHandle vo_handle1 = UTL_GetVoHandle();
UTL_SetVoHigh( vo_handle1, 1.650 V);
UTL_SetVoLow ( vo_handle1, 0.000 V);
UTL_SendVo ( vo_handle1, OUT 1 );
VtHandle vt_handle3 = UTL_GetViHandle();
UTL_SetVt ( vt_handle3, 1.650 V);
UTL_SendVt ( vt_handle3, VT 3 );
Vin : Driver Voltage
Vout : Comparator Reference Voltage
Vterm: 50Ω termination voltage
Vload: 500/1k/2kΩ pull up voltage

## Slide 60: Device Power Supply setting
By using VsHandle, Device Power Supply can be set up.
VsHandle vs_handle_vcc = UTL_GetVsHandle();
UTL_SetVsSource ( vs_handle_vcc, 3.300 V );
UTL_SetVsSrange ( vs_handle_vcc, 4.000 V, 0.000 V);
UTL_SetVsMrange ( vs_handle_vcc, 400.0 mA,-400.0 mA);
UTL_SetVsPclamp ( vs_handle_vcc, 400.0 mA );
UTL_SetVsMclamp ( vs_handle_vcc,-400.0 mA );
UTL_SetVsPhaseCompensation( vs_handle_vcc, UT_DCT_C2 );
UTL_SetVsMeasCnt ( vs_handle_vcc, 1024 );
UTL_SendVs ( vs_handle_vcc, VS 1 );

## Slide 61: To set up High Voltage Driver
UTL_SetPinHvDr(), UTL_SetPinVihhNumber() with PinHandle, VihhMutHandle and VihhHandle are used for High Voltage Driver.
Only even-number pin can be High Voltage Driver
PinHandle pin_handle = UTL_GetPinHandle();
:
UTL_SetPinHvDr ( pin_handle, UT_ON);
UTL_SetPinVihhNumber( pin_handle, 1 );
UTL_SendPin ( pin_handle, "HVPIN");
VihhMutHandle vihh_mut_handle = UTL_GetVihhMutHandle();
UTL_SetVihhMutSignal( vihh_mut_handle, UT_SIG_C(21));
UTL_SendVihhMut ( vihh_mut_handle );
VihhHandle vihh_handle = UTL_GetVihhHandle();
UTL_SetVihhHv ( vihh_handle, 13.000 V);
UTL_SetVihhHigh( vihh_handle, 6.000 V);
UTL_SetVihhLow ( vihh_handle, 0.000 V);
UTL_SendVihh ( vihh_handle, 1 );
W/ C21 VIHH=ON
W/O C21: VIHH=OFF(Normal DR)
VIHH1 use for pins defined as“HVPIN”
VIHH1=ON ... 13 V
VIHH1=OFF... 6V / 0V(Normal DR)
w/ C21
w/o C21
w/o C21

## Slide 62: Pattern Program Setting
By using FctHandle, to select pattern program, to run, to stop and to test with pattern.
FctHandle fct_handle_read_block = UTL_GetFctHandle();
UTL_SetFctMpatName( fct_handle_erase , "pat_nand_flash.mpa");
UTL_SetFctStartPc ( fct_handle_erase , PC 0 );
UTL_MeasFct ( fct_handle_erase );
FctHandle fct_handle_page_program = UTL_GetFctHandle();
UTL_SetFctMpatName( fct_handle_page_program, "pat_nand_flash.mpa");
UTL_SetFctStartPc ( fct_handle_page_program, PC 10 );
UTL_StartFct ( fct_handle_page_program );
FctHandle fct_handle_read_block = UTL_GetFctHandle();
UTL_SetFctMpatName( fct_handle_read_block , "pat_nand_flash.mpa");
UTL_SetFctStartPc ( fct_handle_read_block , PC 20 );
UTL_SetFctNoWait ( fct_handle_read_block , UT_ON );
UTL_StartFct ( fct_handle_read_block );
Test with pattern
Run pattern(Do not distinguish PASS/FAIL)
Run pattern in back ground

## Slide 63: Tips of START PC
START PC must be a number before. But it waste pattern memory and difficult to enlarge a patten. But now you can get the START PC from START LABEL name.
int GetStartPc( const char *pattern_name, const char *start_name)
{
ReadMpatPcHandle read_mpat_pc_handle = UTL_GetReadMpatPcHandle();
  int start_pc;
  UTL_SetReadMpatFileName ( read_mpat_pc_handle, pattern_name);
  UTL_SetReadMpatStartName ( read_mpat_pc_handle, start_name );
UTL_ReadMpatStartPc ( read_mpat_pc_handle, &start_pc );
UTL_DeleteHandle ( read_mpat_pc_handle );
return start_pc;
}

## Slide 64: Test Item Definition
It is necessary to define a function for Each Test-Item to run with an Test-Argument of (void *). And you can run each Test-Item with Test-Name. Test-Name is used for flow-control and showed on Control Panel when it running.
Into Test-Argument, usually put a pointer of structure with test condition such as level, timing, some hardware settings or sub test-items.
UTL_Test( test_handle_erase , "Erase Block 0" );
UTL_Test( test_handle_read , "Read Block 0, Page 0" );
TestHandle test_handle_erase = UTL_GetTestHandle();
TestHandle test_handle_read = UTL_GetTestHandle();
UTL_SetTestAction( test_handle_erase , block_erase_check);
UTL_SetTestArg ( test_handle_erase , test_condition1 );
UTL_SetTestAction( test_handle_read , page_program_check);
UTL_SetTestArg ( test_handle_erase , test_condition2 );
void block_erase_check( void *arg)
{
...
}
To set up test items
Run each items
You can set the pointer of free format argument

## Slide 65: Note of handles
GetHandle() function allocate memory area to save all information to set up. And Send() function set up tester-hardware. Before Send(), hardware setting is keep previous status. And after Send(), even if DeleteHandle() function deletes the handle, hardware setting remain.
And without DeleteHandle() the memory area which GetHandle() allocated are remained. Because always GetHandle() allocate new memory area, it might be the root-cause of memory-leakage.
Always call DeleteHandle() after Send()
Keep handle variables as global, GetHandle() at the beginning of main and do not GetHandle() again, just send it when same settings are necessary
Always use common handle and always start from InitializeHandle() for next setting, even same or different.

## Slide 66: How to write Pattern Program

## Slide 67: ALPG Hardware
ALPG consists 4 parts
  Seqeunce Controller
      This part control the ALPG pattern sequence. All sequences are controlled by Intruction such as NOP, JMP, JSR, RTN, JNIn, IDXIn, FLGLIn, STPS
  Address Generator
      This part calculates X, Y addresses by using several REGISTERs such as XC/YC, XB/YB, XS/YS, XK/YK, XT/YT, XH/YH, B/N, D1, D2, D3, D4 with operators such as <, +, -, *2, /2,
  Data Generator
      This part calculates D, SD data by using several REGISTERs such as TP1, TP2, TPH1, TPH2, D5, D6.
  MUT
      This part input logical data by using MUT such as C0-C31, M1, M2, R, W.

## Slide 68: MPAT and END
MPAT pat_sample
# This is sample code
REGISTER
XMAX = #3FFFF
YMAX = #003FF
IDX1 = #3FFFE
IDX2 = #003FE
START #10
NOP TS1 CYP1 XB<XH YB<YH TP<TPH
ST0: JNI2 ST0 TS1 CYP1 X<XB Y<YB TP<TP+1 R C0
FLGLI1 . TS1 CYP1 X<XB Y<YB YB<YB+1 W C0
STPS
END
Pattern program starts from MPAT statement
Pattern program ends at END statement.

## Slide 69: Pattern file name
MPAT pat_sample
# This is sample code
REGISTER
XMAX = #3FFFF
YMAX = #003FF
IDX1 = #3FFFE
IDX2 = #003FE
START #10
NOP TS1 CYP1 XB<XH YB<YH TP<TPH
ST0: JNI2 ST0 TS1 CYP1 X<XB Y<YB TP<TP+1 R C0
FLGLI1 . TS1 CYP1 X<XB Y<YB YB<YB+1 W C0
STPS
END
Pattern File Name after compile without extension.
Usually put same name of source file name
In this case, target file will be “pat_sample.mpa”

## Slide 70: MPAT program format
MPAT pat_sample
# This is sample code
REGISTER
XMAX = #3FFFF
YMAX = #003FF
IDX1 = #3FFFE
IDX2 = #003FE
START #10
NOP TS1 CYP1 XB<XH YB<YH TP<TPH
ST0: JNI2 ST0 TS1 CYP1 X<XB Y<YB TP<TP+1 R C0
FLGLI1 . TS1 CYP1 X<XB Y<YB YB<YB+1 W C0
STPS
END
Setting Area
Pattern sequence area

## Slide 71: START PC
MPAT pat_sample
# This is sample code
REGISTER
XMAX = #3FFFF
YMAX = #003FF
IDX1 = #3FFFE
IDX2 = #003FE
START #10
NOP TS1 CYP1 XB<XH YB<YH TP<TPH
ST0: JNI2 ST0 TS1 CYP1 X<XB Y<YB TP<TP+1 R C0
FLGLI1 . TS1 CYP1 X<XB Y<YB YB<YB+1 W C0
STPS
END
Pattern sequence always starts from START statement
And following pattern store in the address
#10
#11
#12
ALPG pattern memory
Pattern Count
(Pattern Memory Address)

## Slide 72: Cycles are Line oriented
MPAT pat_sample
# This is sample code
REGISTER
XMAX = #3FFFF
YMAX = #003FF
IDX1 = #3FFFE
IDX2 = #003FE
START #10
NOP TS1 CYP1 XB<XH YB<YH TP<TPH
ST0: JNI2 ST0 TS1 CYP1 X<XB Y<YB TP<TP+1 R C0
FLGLI1 . TS1 CYP1 X<XB Y<YB YB<YB+1 W C0
STPS
END
Pattern program is line based.
One Line = One cycle

## Slide 73: Sequence control part
MPAT pat_sample
# This is sample code
REGISTER
XMAX = #3FFFF
YMAX = #003FF
IDX1 = #3FFFE
IDX2 = #003FE
START #10
NOP TS1 CYP1 XB<XH YB<YH TP<TPH
ST0: JNI2 ST0 TS1 CYP1 X<XB Y<YB TP<TP+1 R C0
FLGLI1 . TS1 CYP1 X<XB Y<YB YB<YB+1 W C0
STPS
END
Sequence Controll part to select the sequence.
NOP ... No Operation, Just go next line
JNIn ... Jump loop with INDEXn(loops IDXn+2)
JMP ... Jump
JSR ... Jump to subroutine.
RTN ... return from subroutine

## Slide 74: Match Polling
MPAT pat_sample
# This is sample code
REGISTER
XMAX = #3FFFF
YMAX = #003FF
IDX1 = #3FFFE
IDX2 = #003FE
START #10
NOP TS1 CYP1 XB<XH YB<YH TP<TPH
ST0: JNI2 ST0 TS1 CYP1 X<XB Y<YB TP<TP+1 R C0
FLGLI1 . TS1 CYP1 X<XB Y<YB YB<YB+1 W C0
STPS
END
Match polling of R/B are done by “FLGLIn m”
Until device output equals to expectation,
pattern jump the label “m”.
FLGLI1 uses IDX8, FLGLI2 uses IDX9...
FLGLIn disable FAIL judgement.

## Slide 75: Labels
MPAT pat_sample
# This is sample code
REGISTER
XMAX = #3FFFF
YMAX = #003FF
IDX1 = #3FFFE
IDX2 = #003FE
START #10
NOP TS1 CYP1 XB<XH YB<YH TP<TPH
ST0: JNI2 ST0 TS1 CYP1 X<XB Y<YB TP<TP+1 R C0
FLGLI1 . TS1 CYP1 X<XB Y<YB YB<YB+1 W C0
STPS
END
“ST0” ... The label to jump
“.” ... Current line(“.-1”:previous line)

## Slide 76: Address Calculation part
MPAT pat_sample
# This is sample code
REGISTER
XMAX = #3FFFF
YMAX = #003FF
IDX1 = #3FFFE
IDX2 = #003FE
START #10
NOP TS1 CYP1 XB<XH YB<YH TP<TPH
ST0: JNI2 ST0 TS1 CYP1 X<XB Y<YB TP<TP+1 R C0
FLGLI1 . TS1 CYP1 X<XB Y<YB YB<YB+1 W C0
STPS
END
Address Calculation part.
Finally X and Y output from ALPG to PDS
X/Y will be changed
at the next cycle of XB/XC/YB/YC register changed

## Slide 77: Data Calculation part
MPAT pat_sample
# This is sample code
REGISTER
XMAX = #3FFFF
YMAX = #003FF
IDX1 = #3FFFE
IDX2 = #003FE
START #10
NOP TS1 CYP1 XB<XH YB<YH TP<TPH
ST0: JNI2 ST0 TS1 CYP1 X<XB Y<YB TP<TP+1 R C0
FLGLI1 . TS1 CYP1 X<XB Y<YB YB<YB+1 W C0
STPS
END
Data Calculation part.
D0-17 and SD0-17 are output from ALPG to PDS.
TP(TP1) and TP2 are source code D0-17 and SD0-17
D-register will be changed at the next cycle of TP register changed

## Slide 78: MUT part
MPAT pat_sample
# This is sample code
REGISTER
XMAX = #3FFFF
YMAX = #003FF
IDX1 = #3FFFE
IDX2 = #003FE
START #10
NOP TS1 CYP1 XB<XH YB<YH TP<TPH
ST0: JNI2 ST0 TS1 CYP1 X<XB Y<YB TP<TP+1 R C0
FLGLI1 . TS1 CYP1 X<XB Y<YB YB<YB+1 W C0
STPS
END
MUT(C0-C31, M0,M1,R,W) or TSn, CYPn are directly output at that cycle

## Slide 79: SDEF
MUT, TSn, CYPn or REGISTER-calculation is not easy to read or understand. SDEF will help to understand easier. SDEF can be written on the top of pattern
SDEF new-mnemonic = mnemonics-already-defined
CS = IN1 /NRZB BCLK1 <C0 > <C0 > <C0 > <C0 > <C0 > <C0 >
CLE = IN2 NRZB BCLK2 <C1 > <C1 > <C1 > <C1 > <C1 > <C1 >
ALE = IN3 NRZB BCLK3 <C2 > <C2 > <C2 > <C2 > <C2 > <C2 >
WE = IN4 /RZO BCLK4 CCLK4 <C3 > <C3 > <C3 > <C3 > <C3 > <C3 >
RE = IN5 /RZO BCLK5 CCLK5 <C4 > <C4 > <C4 > <C4 > <C4 > <C4 >
WP = IN6 FIXH
DQ7 = IN7 NRZB BCLK7 IOC DRE1 DRECLK1 DRENRZ OUT1 STRB1 EXPA1 <Y7 > <FL > <X7 > <X15> <FL > <D7 >
DQ6 = IN7 NRZB BCLK7 IOC DRE1 DRECLK1 DRENRZ OUT1 STRB1 EXPA1 <Y6 > <FL > <X6 > <X14> <FL > <D6 >
DQ5 = IN7 NRZB BCLK7 IOC DRE1 DRECLK1 DRENRZ OUT1 STRB1 EXPA1 <Y5 > <Y13> <X5 > <X13> <FL > <D5 >
DQ4 = IN7 NRZB BCLK7 IOC DRE1 DRECLK1 DRENRZ OUT1 STRB1 EXPA1 <Y4 > <Y12> <X4 > <X12> <FL > <D4 >
DQ3 = IN7 NRZB BCLK7 IOC DRE1 DRECLK1 DRENRZ OUT1 STRB1 EXPA1 <Y3 > <Y11> <X3 > <X11> <FL > <D3 >
DQ2 = IN7 NRZB BCLK7 IOC DRE1 DRECLK1 DRENRZ OUT1 STRB1 EXPA1 <Y2 > <Y10> <X2 > <X19> <X18> <D2 >
DQ1 = IN7 NRZB BCLK7 IOC DRE1 DRECLK1 DRENRZ OUT1 STRB1 EXPA1 <Y1 > <Y9 > <X1 > <X8 > <X17> <D1 >
DQ0 = IN7 NRZB BCLK7 IOC DRE1 DRECLK1 DRENRZ OUT1 STRB1 EXPA1 <Y0 > <Y8 > <X0 > <X7 > <X16> <D0 >
; CS CLE ALE WE RE DRE CPE
SDEF CMD = CYP6 C0 C1 C3 W
SDEF NOP = CYP1 C0
SDEF ADR1 = CYP1 C0 C2 C3 W
SDEF ADR2 = CYP2 C0 C2 C3 W
SDEF ADR3 = CYP3 C0 C2 C3 W
SDEF ADR4 = CYP4 C0 C2 C3 W
SDEF ADR5 = CYP5 C0 C2 C3 W
SDEF DIN = CYP6 C0 C3 W
SDEF DOUT = CYP6 C0 C4 R

## Slide 80: Example to write pattern program
From here, learn how to write pattern with this erase pattern.
MPAT pat_nandflash
; CS CLE ALE WE RE DRE CPE
SDEF CMD = CYP6 C0 C1 C3 W
SDEF NOP = CYP1 C0
SDEF ADR1 = CYP1 C0 C2 C3 W
SDEF ADR2 = CYP2 C0 C2 C3 W
SDEF ADR3 = CYP3 C0 C2 C3 W
SDEF ADR4 = CYP4 C0 C2 C3 W
SDEF ADR5 = CYP5 C0 C2 C3 W
SDEF DIN = CYP6 C0 C3 W
SDEF DOUT = CYP6 C0 C4 R
REGISTER
START #0
STPS
END
Pattern will be written
between START and STPS

## Slide 81: Example to write pattern program
First cycle and Command input cycle.
MPAT pat_nandflash
; CS CLE ALE WE RE DRE CPE
SDEF CMD = CYP6 C0 C1 C3 W
SDEF NOP = CYP1 C0
SDEF ADR1 = CYP1 C0 C2 C3 W
SDEF ADR2 = CYP2 C0 C2 C3 W
SDEF ADR3 = CYP3 C0 C2 C3 W
SDEF ADR4 = CYP4 C0 C2 C3 W
SDEF ADR5 = CYP5 C0 C2 C3 W
SDEF DIN = CYP6 C0 C3 W
SDEF DOUT = CYP6 C0 C4 R
REGISTER
START #0
NOP TS1 TP1<#60
NOP TS1 CMD
STPS
END
The 60h also input from D-register, and
TP register must be set previously.

## Slide 82: Example to write pattern program
Address input cycles
MPAT pat_nandflash
; CS CLE ALE WE RE DRE CPE
SDEF CMD = CYP6 C0 C1 C3 W
SDEF NOP = CYP1 C0
SDEF ADR1 = CYP1 C0 C2 C3 W
SDEF ADR2 = CYP2 C0 C2 C3 W
SDEF ADR3 = CYP3 C0 C2 C3 W
SDEF ADR4 = CYP4 C0 C2 C3 W
SDEF ADR5 = CYP5 C0 C2 C3 W
SDEF DIN = CYP6 C0 C3 W
SDEF DOUT = CYP6 C0 C4 R
REGISTER
START #0
NOP TS1 XB<XH TP1<#60
NOP TS1 CMD X<XB
NOP TS1 ADR3 X<XB
NOP TS1 ADR4 X<XB
NOP TS1 ADR5 X<XB
STPS
END
R1～R3 addresses input cycles
X is assigned for XB and XB initialized with XH

## Slide 83: Example to write pattern program
Second command input cycle
MPAT pat_nandflash
; CS CLE ALE WE RE DRE CPE
SDEF CMD = CYP6 C0 C1 C3 W
SDEF NOP = CYP1 C0
SDEF ADR1 = CYP1 C0 C2 C3 W
SDEF ADR2 = CYP2 C0 C2 C3 W
SDEF ADR3 = CYP3 C0 C2 C3 W
SDEF ADR4 = CYP4 C0 C2 C3 W
SDEF ADR5 = CYP5 C0 C2 C3 W
SDEF DIN = CYP6 C0 C3 W
SDEF DOUT = CYP6 C0 C4 R
REGISTER
START #0
NOP TS1 XB<XH TP1<#60
NOP TS1 CMD
NOP TS1 ADR3 X<XB
NOP TS1 ADR4 X<XB
NOP TS1 ADR5 X<XB TP1<#D0
NOP TS1 CMD
STPS
END
The D0h also input from D-register, and
TP register must be set previously.

## Slide 84: Example to write pattern program
To take care about tWB(WE# High to R/B# LOW time)
MPAT pat_nandflash
; CS CLE ALE WE RE DRE CPE
SDEF CMD = CYP6 C0 C1 C3 W
SDEF NOP = CYP1 C0
SDEF ADR1 = CYP1 C0 C2 C3 W
SDEF ADR2 = CYP2 C0 C2 C3 W
SDEF ADR3 = CYP3 C0 C2 C3 W
SDEF ADR4 = CYP4 C0 C2 C3 W
SDEF ADR5 = CYP5 C0 C2 C3 W
SDEF DIN = CYP6 C0 C3 W
SDEF DOUT = CYP6 C0 C4 R
REGISTER
START #0
NOP TS1 XB<XH TP1<#60
NOP TS1 CMD
NOP TS1 ADR3 X<XB
NOP TS1 ADR4 X<XB
NOP TS1 ADR5 X<XB TP1<#D0
NOP TS1 CMD
NOP TS1 NOP
NOP TS1 NOP
STPS
END
Because tWB=200ns, put 2 cycles here
(RATE<1>=100ns)

## Slide 85: Example to write pattern program
Wait until all device are ready for previous command.
MPAT pat_nandflash
; CS CLE ALE WE RE DRE CPE
SDEF CMD = CYP6 C0 C1 C3 W
SDEF NOP = CYP1 C0
SDEF ADR1 = CYP1 C0 C2 C3 W
SDEF ADR2 = CYP2 C0 C2 C3 W
SDEF ADR3 = CYP3 C0 C2 C3 W
SDEF ADR4 = CYP4 C0 C2 C3 W
SDEF ADR5 = CYP5 C0 C2 C3 W
SDEF DIN = CYP6 C0 C3 W
SDEF DOUT = CYP6 C0 C4 R
REGISTER
START #0
NOP TS1 XB<XH TP1<#60
NOP TS1 CMD
NOP TS1 ADR3 X<XB
NOP TS1 ADR4 X<XB
NOP TS1 ADR5 X<XB TP1<#D0
NOP TS1 CMD
NOP TS1 NOP
NOP TS1 NOP
FLGLI1 . TS2 NOP
STPS
END
Match polling here

## Slide 86: Example to write pattern program
Handles polling fails
MPAT pat_nandflash
; CS CLE ALE WE RE DRE CPE
SDEF CMD = CYP6 C0 C1 C3 W
SDEF NOP = CYP1 C0
SDEF ADR1 = CYP1 C0 C2 C3 W
SDEF ADR2 = CYP2 C0 C2 C3 W
SDEF ADR3 = CYP3 C0 C2 C3 W
SDEF ADR4 = CYP4 C0 C2 C3 W
SDEF ADR5 = CYP5 C0 C2 C3 W
SDEF DIN = CYP6 C0 C3 W
SDEF DOUT = CYP6 C0 C4 R
REGISTER
BAR = RBFAIL
START #0
NOP TS1 XB<XH TP1<#60
NOP TS1 CMD
NOP TS1 ADR3 X<XB
NOP TS1 ADR4 X<XB
NOP TS1 ADR5 X<XB TP1<#D0
NOP TS1 CMD
NOP TS1 NOP
NOP TS1 NOP
FLGLI1 . TS2 NOP
STPS
RBFAIL: NOP
STFL
END
Put the label name when polling failed.
When polling overflow(loop counts over IDX8),
FLGLI1 jump into BAR registered label.
This sample does “Set FAIL” with STFL command.

## Slide 87: DC testing

## Slide 88: Outline
DC (Direct Current) unit has 2 function. First one is provide voltage or current source into signal line. Another is measure voltage or current of signal line. DC unit will be helpful for continuity-check with device, leakage or monitor device output.
  For Continuity check(Contact check, Open/short check)
      ISVM (Current Source Voltage Measure) is used for this purpose. With Voltage-Source, If short-circuit happens, large current flow it may damage on device, socket or probe-card. We can find both of open-fail device and short-fail device.
  For Leakage check
      VSIM (Voltage Source Current Measure) is used for this purpose. After continuity check, voltage-source test is safe for this device.
  For Monitor
      ISVM (Current Source Voltage Measure) with 0A is used for this purpose.

## Slide 89: How to set up
DcHandle can set up DC unit - DC mode, Source, Range of Source and Measurement, Limit of PASS RANGE, measurement count and Clamps.
DcHandle dc_handle_isvm = UTL_GetDcHandle();
UTL_SetDcMode ( dc_handle_isvm, UTD_ISVM );
UTL_SetDcSource ( dc_handle_isvm, -10.00 uA );
UTL_SetDcSrange ( dc_handle_isvm, 0.000 uA, -100.0 uA);
UTL_SetDcMrange ( dc_handle_isvm, 0.000 V, -1.000 V);
UTL_SetDcLimitHigh( dc_handle_isvm, -100.0 mV, UT_ON );
UTL_SetDcLimitLow ( dc_handle_isvm, -1.900 V, UT_ON );
UTL_SetDcMeasCnt ( dc_handle_isvm, 16 );
UTL_SetDcPclamp ( dc_handle_isvm, 0.600 V );
UTL_SetDcMclamp ( dc_handle_isvm, -1.200 V );
UTL_SendDc ( dc_handle_isvm );
DcHandle dc_handle_vsim = UTL_GetDcHandle();
UTL_SetDcMode ( dc_handle_vsim, UTD_VSIM );
UTL_SetDcSource ( dc_handle_vsim, +3.300 V );
UTL_SetDcSrange ( dc_handle_vsim, +4.000 V, 0.0 V);
UTL_SetDcMrange ( dc_handle_vsim, +100.0 uA, -100.0 uA);
UTL_SetDcLimitHigh( dc_handle_vsim, +10.00 uA, UT_ON );
UTL_SetDcLimitLow ( dc_handle_vsim, -10.00 uA, UT_ON );
UTL_SetDcMeasCnt ( dc_handle_isvm, 1024 );
UTL_SendDc ( dc_handle_vsim );
This is used for continuity check
This is used for leakage check

## Slide 90: Settling time of DC unit
The settling-time of current, voltage depends on the balance between current of DC unit and load of device. SettlingTimeHandle can set up the settling time of DC unit after connection inside of measurement function.
SettlingHandle settling_handle = UTL_GetSettlingHandle();
UTL_SetSettlingTime ( settling_handle, 3.000 ms);
UTL_SetSettlingTimeAfterRon( settling_handle, 1.000 ms);
UTL_SetSettlingTimeAfterRof( settling_handle, 1.000 ms);
UTL_SendSettlingTime ( settling_handle );

## Slide 91: DC testing
DctHandle can test with DC unit. DC unit setting must be done before call “UTL_MeasDct()”. If necessary, start pattern and wait enough time for device to be before UTL_MeasDct()
DctHandle is used for ICC test. After set up VsHandle, run UTL_MeasDct() with the pinlist of VS.
DctHandle dct_handle = UTL_GetDctHandle();
UTL_SetDctPinList ( dct_handle, "ALLPIN");
// Reference-on or pattern start here, if necessary
UTL_MeasDct ( dct_handle );
// pattern stop here, if started and not necessary anymore

## Slide 92: DUT access / PIN access
DutCursor can used for accesssing each DUT and PinCursor can used for accessing each PIN. The memory area is allocated for each cursor, that’s why it is necessary to delete each time after used.
DutCursor dut_cursor = UTL_GetDutCursor( UT_CDUT) {
UT_DUT dut;
while( (dut = UTL_NextDut( dut_cursor)) != UT_NOMORE ) {
PinCursor pin_cursor = UTL_GetPinCursor( "DQ");
UT_PIN pin;
while( (pin = UTL_NextPin( pin_cursor)) != UT_NOMORE ) {
// Something for each DUT & each PIN
}
UTL_DeleteCursor( pin_cursor);
}
UTL_DeleteCursor( dut_cursor);
DDUT All Dut defined in socket file
SDUT All DUT set by prober or handler
CDUT All target DUT now
PDUT All Passed DUT at previous MEAS
FDUT All Failed DUT at previous MEAS
PINLIST name
Always Need to delete each time after used

## Slide 93: Optional Units

## Slide 94: How to Use DBM

## Slide 95: Outline
DBM(Data Buffer Memory) is the unit to generate vector pattern. Data is transferred to DBM before measurement, and issued by controlling ALPG. DBM has 2 modes.
DBM output the data sequentially. ALPG control DBM AP(address pointer) by DBMINC. By using BM(Buffer Memory), 800Mbps is realized. On the other hand transfer time (from DBM to BM) is required for each 32K. Density is 64MW.

## Slide 96: Block Diagram of DBM (AP mode)
DBM data is stored before measurement.
ALPG issue DBMXFER + DBMAP
DBM start to transfer data to BM
ALPG wait complete the data transfer by JBF.
ALPG issue data & control BM address by DBMINC.
ALPG issue can inhibit DBM output for each cycles
FC
ALPG
DBM
(64MW)
BM
(32KW)
DBM AP
Test
Processor
②DBMXFER
④ JBF
⑤DBMINC(BMINC)
DBM address
③Transfer DBM data
①Store DBM data
⑥INHDBM
⑥ ALPG pattern outputs with INHDBM
MPAT pat
MODE DBMXFER
REGISTER
DBMA = #0
START #0
NOP DBMXFER
JBF .
…
NOP
JNI . DBMINC
NOP INHDBM
…
STPS INHDBM
END
③
④
⑤
⑥

## Slide 97: How to set up DBM
DbmConfigHandle can set up DBM configurations
DbmConfigHandle dbm_config_handle = UTL_GetDbmConfigHandle();
UTL_SetDbmConfigAccessMode( dbm_config_handle, UT_DBM_ACCESS_AP);
UTL_SetDbmConfigBitSize ( dbm_config_handle, 12 IO );
UTL_AddDbmConfigPinAssign ( dbm_config_handle, PIN 33 );
UTL_AddDbmConfigPinAssign ( dbm_config_handle, PIN 34 );
UTL_AddDbmConfigPinAssign ( dbm_config_handle, PIN 35 );
UTL_AddDbmConfigPinAssign ( dbm_config_handle, PIN 36 );
UTL_AddDbmConfigPinAssign ( dbm_config_handle, PIN 37 );
UTL_AddDbmConfigPinAssign ( dbm_config_handle, PIN 38 );
UTL_AddDbmConfigPinAssign ( dbm_config_handle, PIN 39 );
UTL_AddDbmConfigPinAssign ( dbm_config_handle, PIN 40 );
UTL_AddDbmConfigPinAssign ( dbm_config_handle, PIN 49 );
UTL_AddDbmConfigPinAssign ( dbm_config_handle, PIN 51 );
UTL_SendDbmConfig ( dbm_config_handle );

## Slide 98: Data Write to DBM
DbmAccessHandle cam access tp DBM memory
#define DBM_DATA_COUNT 8640
unsigned int dbm_data[ DBM_DATA_COUNT/2];
int i;
for ( i=0; i<DBM_DATA_COUNT/2; i++) { dbm_data[i] = (0xAA << 12) | 0x55; }
DbmAccessHandle dbm_access_handle = UTL_GetDbmAccessHandle();
UTL_SetDbmAccessAllUnit ( dbm_access_handle, UT_ON );
UTL_SetDbmAccessDataKind ( dbm_access_handle, UT_DBM_PPAT );
UTL_SetDbmAccessAllBlock ( dbm_access_handle, UT_ON );
UTL_SetDbmAccessStartAddr( dbm_access_handle, 0 );
UTL_SetDbmAccessStopAddr ( dbm_access_handle, sizeof dbm_data-1 );
UTL_WriteDbm ( dbm_access_handle, dbm_data, sizeof dbm_data);

## Slide 99: DBM Format(24bit)
Write DBM | 1WAY SDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 09 | 08 | 07 | 06 | 05 | 04 | 03 | 02 | 01 | 00
dbm_data[ 0] |  |  |  |  |  |  |  |  | 1st cycle |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
dbm_data[ 1] |  |  |  |  |  |  |  |  | 2nd cycle |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
dbm_data[ 2] |  |  |  |  |  |  |  |  | 3rd cycle |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
dbm_data[ 3] |  |  |  |  |  |  |  |  | 4th cycle |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Write DBM | 1WAY DDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 09 | 08 | 07 | 06 | 05 | 04 | 03 | 02 | 01 | 00
dbm_data[ 0] |  |  |  |  |  |  |  |  | 1st cycle / 1st half of DDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
dbm_data[ 1] |  |  |  |  |  |  |  |  | 1st cycle / 2nd half of DDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
dbm_data[ 2] |  |  |  |  |  |  |  |  | 2nd cycle / 1st half of DDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
dbm_data[ 3] |  |  |  |  |  |  |  |  | 2nd cycle / 2nd half of DDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Write DBM | 2WAY SDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 09 | 08 | 07 | 06 | 05 | 04 | 03 | 02 | 01 | 00
dbm_data[ 0] |  |  |  |  |  |  |  |  | 1st cycle |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
dbm_data[ 1] |  |  |  |  |  |  |  |  | 2nd cycle |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
dbm_data[ 2] |  |  |  |  |  |  |  |  | 3rd cycle |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
dbm_data[ 3] |  |  |  |  |  |  |  |  | 4th cycle |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Write DBM | 2WAY DDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 09 | 08 | 07 | 06 | 05 | 04 | 03 | 02 | 01 | 00
dbm_data[ 0] |  |  |  |  |  |  |  |  | 1st cycle / 1st half of DDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
dbm_data[ 1] |  |  |  |  |  |  |  |  | 1st cycle / 2nd half of DDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
dbm_data[ 2] |  |  |  |  |  |  |  |  | 2nd cycle / 1st half of DDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
dbm_data[ 3] |  |  |  |  |  |  |  |  | 2nd cycle / 2nd half of DDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Blue frame = 1 instruction

## Slide 100: DBM Format(12bit)
Write DBM | 1WAY SDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 09 | 08 | 07 | 06 | 05 | 04 | 03 | 02 | 01 | 00
dbm_data[ 0] |  |  |  |  |  |  |  |  | 2nd cycle |  |  |  |  |  |  |  |  |  |  |  | 1st cycle |  |  |  |  |  |  |  |  |  |  | 
dbm_data[ 1] |  |  |  |  |  |  |  |  | 4th cycle |  |  |  |  |  |  |  |  |  |  |  | 3rd cycle |  |  |  |  |  |  |  |  |  |  | 
dbm_data[ 2] |  |  |  |  |  |  |  |  | 6th cycle |  |  |  |  |  |  |  |  |  |  |  | 5th cycle |  |  |  |  |  |  |  |  |  |  | 
dbm_data[ 3] |  |  |  |  |  |  |  |  | 8th cycle |  |  |  |  |  |  |  |  |  |  |  | 7th cycle |  |  |  |  |  |  |  |  |  |  | 
Write DBM | 1WAY DDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 09 | 08 | 07 | 06 | 05 | 04 | 03 | 02 | 01 | 00
dbm_data[ 0] |  |  |  |  |  |  |  |  | 1st cycle / 2nd half |  |  |  |  |  |  |  |  |  |  |  | 1st cycle / 1st half |  |  |  |  |  |  |  |  |  |  | 
dbm_data[ 1] |  |  |  |  |  |  |  |  | 2nd cycle / 2nd half |  |  |  |  |  |  |  |  |  |  |  | 2nd cycle / 1st half |  |  |  |  |  |  |  |  |  |  | 
dbm_data[ 2] |  |  |  |  |  |  |  |  | 3rd cycle / 2nd half |  |  |  |  |  |  |  |  |  |  |  | 3rd cycle / 1st half |  |  |  |  |  |  |  |  |  |  | 
dbm_data[ 3] |  |  |  |  |  |  |  |  | 4th cycle / 2nd half |  |  |  |  |  |  |  |  |  |  |  | 4th cycle / 1st half |  |  |  |  |  |  |  |  |  |  | 
Write DBM | 2WAY SDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 09 | 08 | 07 | 06 | 05 | 04 | 03 | 02 | 01 | 00
dbm_data[ 0] |  |  |  |  |  |  |  |  | 2nd cycle |  |  |  |  |  |  |  |  |  |  |  | 1st cycle |  |  |  |  |  |  |  |  |  |  | 
dbm_data[ 1] |  |  |  |  |  |  |  |  | 4th cycle |  |  |  |  |  |  |  |  |  |  |  | 3rd cycle |  |  |  |  |  |  |  |  |  |  | 
dbm_data[ 2] |  |  |  |  |  |  |  |  | 6th cycle |  |  |  |  |  |  |  |  |  |  |  | 5th cycle |  |  |  |  |  |  |  |  |  |  | 
dbm_data[ 3] |  |  |  |  |  |  |  |  | 8th cycle |  |  |  |  |  |  |  |  |  |  |  | 7th cycle |  |  |  |  |  |  |  |  |  |  | 
Write DBM | 2WAY DDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 09 | 08 | 07 | 06 | 05 | 04 | 03 | 02 | 01 | 00
dbm_data[ 0] |  |  |  |  |  |  |  |  | 1st cycle / 2nd half |  |  |  |  |  |  |  |  |  |  |  | 1st cycle / 1st half |  |  |  |  |  |  |  |  |  |  | 
dbm_data[ 1] |  |  |  |  |  |  |  |  | 2nd cycle / 2nd half |  |  |  |  |  |  |  |  |  |  |  | 2nd cycle / 1st half |  |  |  |  |  |  |  |  |  |  | 
dbm_data[ 2] |  |  |  |  |  |  |  |  | 3rd cycle / 2nd half |  |  |  |  |  |  |  |  |  |  |  | 3rd cycle / 1st half |  |  |  |  |  |  |  |  |  |  | 
dbm_data[ 3] |  |  |  |  |  |  |  |  | 4th cycle / 2nd half |  |  |  |  |  |  |  |  |  |  |  | 4th cycle / 1st half |  |  |  |  |  |  |  |  |  |  | 

## Slide 101: DBM Format(6bit)
Write DBM | 1WAY SDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 09 | 08 | 07 | 06 | 05 | 04 | 03 | 02 | 01 | 00
dbm_data[ 0] |  |  |  |  |  |  |  |  | 4th cycle |  |  |  |  |  | 3rd cycle |  |  |  |  |  | 2nd cycle |  |  |  |  |  | 1st cycle |  |  |  |  | 
dbm_data[ 1] |  |  |  |  |  |  |  |  | 8th cycle |  |  |  |  |  | 7th cycle |  |  |  |  |  | 6th cycle |  |  |  |  |  | 5th cycle |  |  |  |  | 
dbm_data[ 2] |  |  |  |  |  |  |  |  | 12th cycle |  |  |  |  |  | 11th cycle |  |  |  |  |  | 10th cycle |  |  |  |  |  | 9th cycle |  |  |  |  | 
dbm_data[ 3] |  |  |  |  |  |  |  |  | 16th cycle |  |  |  |  |  | 15th cycle |  |  |  |  |  | 14th cycle |  |  |  |  |  | 13th cycle |  |  |  |  | 
Write DBM | 1WAY DDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 09 | 08 | 07 | 06 | 05 | 04 | 03 | 02 | 01 | 00
dbm_data[ 0] |  |  |  |  |  |  |  |  | 2nd cycle / 2nd half |  |  |  |  |  | 2nd cycle / 1st half |  |  |  |  |  | 1st cycle / 2nd half |  |  |  |  |  | 1st cycle / 1st half |  |  |  |  | 
dbm_data[ 1] |  |  |  |  |  |  |  |  | 4th cycle / 2nd half |  |  |  |  |  | 4th cycle / 1st half |  |  |  |  |  | 3rd cycle / 2nd half |  |  |  |  |  | 3rd cycle / 1st half |  |  |  |  | 
dbm_data[ 2] |  |  |  |  |  |  |  |  | 6th cycle / 2nd half |  |  |  |  |  | 6th cycle / 1st half |  |  |  |  |  | 5th cycle / 2nd half |  |  |  |  |  | 5th cycle / 1st half |  |  |  |  | 
dbm_data[ 3] |  |  |  |  |  |  |  |  | 8th cycle / 2nd half |  |  |  |  |  | 8th cycle / 1st half |  |  |  |  |  | 7th cycle / 2nd half |  |  |  |  |  | 7th cycle / 1st half |  |  |  |  | 
Write DBM | 2WAY SDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 09 | 08 | 07 | 06 | 05 | 04 | 03 | 02 | 01 | 00
dbm_data[ 0] |  |  |  |  |  |  |  |  | 4th cycle |  |  |  |  |  | 3rd cycle |  |  |  |  |  | 2nd cycle |  |  |  |  |  | 1st cycle |  |  |  |  | 
dbm_data[ 1] |  |  |  |  |  |  |  |  | 8th cycle |  |  |  |  |  | 7th cycle |  |  |  |  |  | 6th cycle |  |  |  |  |  | 5th cycle |  |  |  |  | 
dbm_data[ 2] |  |  |  |  |  |  |  |  | 12th cycle |  |  |  |  |  | 11th cycle |  |  |  |  |  | 10th cycle |  |  |  |  |  | 9th cycle |  |  |  |  | 
dbm_data[ 3] |  |  |  |  |  |  |  |  | 16th cycle |  |  |  |  |  | 15th cycle |  |  |  |  |  | 14th cycle |  |  |  |  |  | 13th cycle |  |  |  |  | 
Write DBM | 2WAY DDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 09 | 08 | 07 | 06 | 05 | 04 | 03 | 02 | 01 | 00
dbm_data[ 0] |  |  |  |  |  |  |  |  | 2nd cycle / 2nd half |  |  |  |  |  | 2nd cycle / 1st half |  |  |  |  |  | 1st cycle / 2nd half |  |  |  |  |  | 1st cycle / 1st half |  |  |  |  | 
dbm_data[ 1] |  |  |  |  |  |  |  |  | 4th cycle / 2nd half |  |  |  |  |  | 4th cycle / 1st half |  |  |  |  |  | 3rd cycle / 2nd half |  |  |  |  |  | 3rd cycle / 1st half |  |  |  |  | 
dbm_data[ 2] |  |  |  |  |  |  |  |  | 6th cycle / 2nd half |  |  |  |  |  | 6th cycle / 1st half |  |  |  |  |  | 5th cycle / 2nd half |  |  |  |  |  | 5th cycle / 1st half |  |  |  |  | 
dbm_data[ 3] |  |  |  |  |  |  |  |  | 8th cycle / 2nd half |  |  |  |  |  | 8th cycle / 1st half |  |  |  |  |  | 7th cycle / 2nd half |  |  |  |  |  | 7th cycle / 1st half |  |  |  |  | 

## Slide 102: How to use UBM

## Slide 103: Outline
The UBM (Universal Buffer Memory) is the function that mainly generates individual Driver Pattern and Expected Pattern to each DUT and Captures fail data. There are no restriction about test speed. It can be used for Reading out device ID, Inputting trimming data, etc.
Generate individual Driver Patterns
Generate individual Expected Pattern
The UBM of T5830 can use every DR pins and IO pins and can use both SDR and DDR. The UBM Capacity of T5830 is 16K words.

## Slide 104: Block Diagram of UBM
UBM is controlled by 2 kind of MUT.
UBM enable
Initialize UBM-AP(UBM Address Pointer)
Functional Block Diagram of the UBM
PDS
ALPG
TG control signal
APLG Pattern Data
MUT
UBM
S
R
ADDRESS
POINTER
CONT
MUT
32KW
sel
mode sel
TG &
Main FC
Sub
FC
Logic
Comparator
< PIN >
MUT
DR
CP
AFM
Address
Fail address
UBM address
UBM enable
Generate Waveform
NRZB
RZO
RZZ
DNRZ
/NRZB
/RZO
/RZZ
/DNRZ

## Slide 105: UBM setting
UbmConfigHandle is used for setting up UBM
UbmConfigHandle ubm_config_handle = UTL_GetUbmConfigHandle();
// Select the purpose of UBM
// Pattern Generator(UT_UBM_UNIT_PM) or Expected data for Reading(UT_UBM_UNIT_EXP)
// Select MUT signal to enable UBM
UTL_AddUbmConfigFunctionSelect( ubm_config_handle, UT_UBM_UNIT_PM, UT_SIG_C(20));
// Select PINLIST to use UBM
UTL_SetUbmConfigPin ( ubm_config_handle, UT_UBM_UNIT_PM, "DQ" );
// Set up the Jump Address of UBM-AP
UTL_SetUbmConfigJumpAddr ( ubm_config_handle, UT_UBM_UNIT_PM, 0, UBMAP 0 );
// Set up the MUT signal to Jump UBM-AP
UTL_SetUbmConfigJumpCycle ( ubm_config_handle, UT_UBM_UNIT_PM, 0, UT_SIG_C(21));
// Always use UBM as DR pattern
UTL_SetUbmConfigPmMode ( ubm_config_handle, UT_UBM_MODE_DRPAT );
UTL_SendUbmConfig ( ubm_config_handle );

## Slide 106: Write Data into UBM
UbmAccessHandle is used to write data into UBM.
UbmAccessHandle ubm_access_handle = UTL_GetUbmAccessHandle();
#define UBM_DATA_COUNT 8640
unsigned int ubm_data[ UBM_DATA_COUNT];
int i;
for ( i=0; i<UBM_DATA_COUNT/2; i++) { ubm_data[2*i+0] = 0x55000000; ubm_data[2*i+1] = 0xAA000000;}
// Select DUT to write UBM
UTL_SetUbmAccessDut ( ubm_access_handle, dut );
// Select PINLIST to write UBM
UTL_SetUbmAccessPin ( ubm_access_handle, "DQ" );
// Set up Start Address to write UBM
UTL_SetUbmAccessStartAddr( ubm_access_handle, 0 );
// Set up Stop Address to write UBM
UTL_SetUbmAccessStopAddr ( ubm_access_handle, UBM_DATA_COUN-1 );
// Select the buffer stored UBM data to copy.
UTL_WriteUbm ( ubm_access_handle, ubm_data, sizeof ubm_data);

## Slide 107: UBM data format
In UBM data format, data bits correspond to the bit (D0-Dn) of the pin to be accessed from the most significant bit to the least significant bit.
For example, the case that IO pins with BIT=10 are used like right socket program is shown.
Socket program
UBM data format
SOCKET soc
DEFINE MULTIPLE 2DUT 1SITE
BIT=10
PPS=1
DUT# = VS1, P33-40, P49, P51
DUT1 = PPS1A P33-40A, P49A, P51A
DUT2 = PPS1A P41-48A, P53A, P55A
END
UTL_CreatePinlist ( "DQ");
UTL_SetPinType ( "DQ", UT_PINTYPE_PIN);
UTL_AddPinNumber ( "DQ", 33 );
UTL_AddPinNumber ( "DQ", 34 );
UTL_AddPinNumber ( "DQ", 35 );
UTL_AddPinNumber ( "DQ", 36 );
UTL_AddPinNumber ( "DQ", 37 );
UTL_AddPinNumber ( "DQ", 38 );
UTL_AddPinNumber ( "DQ", 39 );
UTL_AddPinNumber ( "DQ", 40 );
UTL_AddPinNumber ( "DQ", 49 );
UTL_AddPinNumber ( "DQ", 51 );
UTL_SetUbmAccessPin( ubm_access_handle, "DQ");
Example of PINLIST

## Slide 108: UBM Address
Note that addressing of UBM are different depending on the interleave mode and SDR/DDR. UBM start address(STADR) and jump address also follow this rule. Relationship of the array variable and UBM address is as follows.
In case of ILMODE 1WAY and SDR mode
In case of ILMODE 2WAY and SDR mode
Array | Cycle | DDR | UBM address
ubm_data[0] | 1st |  | 0
ubm_data[1] | 2nd |  | 1
ubm_data[2] | 3rd |  | 2
ubm_data[3] | 4th |  | 3
ubm_data[4] | 5th |  | 4
Array | Cycle | DDR | UBM address
ubm_data[0] | 1st | 1st half | 0
ubm_data[1] | 1st | 2nd half | 0
ubm_data[2] | 2nd | 1st half | 1
ubm_data[3] | 2nd | 2nd half | 1
ubm_data[4] | 3rd | 1st half | 2
Array | Cycle | DDR | UBM address
ubm_data[0] | 1st |  | 0
ubm_data[1] | 2nd |  | 0
ubm_data[2] | 3rd |  | 1
ubm_data[3] | 4th |  | 1
ubm_data[4] | 5th |  | 2
Array | Cycle | DDR | UBM address
ubm_data[0] | 1st | 1st half | 0
ubm_data[1] | 1st | 2nd half | 0
ubm_data[2] | 2nd | 1st half | 0
ubm_data[3] | 2nd | 2nd half | 0
ubm_data[4] | 3rd | 1st half | 1
In case of ILMODE 1WAY and DDR mode
In case of ILMODE 2WAY and DDR mode

## Slide 109: Sample Pattern
Sample pattern program for Individual DR pattern generation
MPAT pat_nandflash
SDEF UBM_ENB = C20
SDEF UBM_CLR = C21
START #20
NOP TS1 XB<XH TP1<#80
NOP TS1 CMD
NOP TS1 ADR1 X<XB
NOP TS1 ADR2 X<XB
NOP TS1 ADR3 X<XB
NOP TS1 ADR4 X<XB
NOP TS1 ADR5 X<XB TP1<#D0
NOP TS1 NOP
NOP TS1 NOP
NOP TS1 CMD UBM_CLR
JNI1 . TS1 DIN TP1<#11 UBM_ENB
NOP TS1 CMD
NOP TS1 NOP
NOP TS1 NOP
FLGLI1 . TS2 NOP
STPS
RBFAIL: NOP
STFL
END
Jump UBMAP
Enable UBM and increase UBMAP

## Slide 110: UBM tool
The UBM tool shows the contents of UBM and enable to edit data.

## Slide 111: How to use BBM

## Slide 112: Outline
BBM(Bad Block Memory) stores Pass/Fail information for each Block. BBM can reduce test-time. When MEAS MPAT failed, BBM capture the Bad Block information. Tester doesn’t write any data into the Bad Block, and also Ready/Busy doesn’t wait for the Bad Block to reduce test-time.
PG
DUT1
DUT2
DUT3
DUT4
DUT16
CP
DR
Address
Address
Block MASK
Bad Block Capture
････
････
････
････
････
DUT1
DUT2
DUT3
DUT4
DUT8
Block0
Block1
Block2
Block3
Block4
Blockn
････
････
････
････
････
････
････
････
Good
Good
Good
Good
Good
Block0
････
Bad Block Memory
I/O ｘ16
Bad Block Memory
Good
Good
Good
Good
Good
Block1
Good
Good
Bad
Good
Good
Good
Good
Bad
Good
Good
Block2
Good
Good
Good
Good
Good
Good
Good
Good
Good
Good
Block3
Good
Good
Good
Bad
Good
Good
Good
Good
Bad
Good
Block4
Bad
Good
Good
Bad
Good
Bad
Good
Good
Bad
Good
Good
Good
Good
Good
Good
TEST
TEST
TEST
TEST
TEST
Block0
Good
Good
Good
Good
Good
Good
Good
Good
Good
Good
Good
Good
Bad
Good
Good
Block1
TEST
TEST
Mask
TEST
TEST
Good
Good
Bad
Good
Good
Block2
TEST
TEST
TEST
TEST
TEST
Good
Good
Good
Good
Good
Good
Good
Good
Good
Bad
Block3
Good
Good
Good
Bad
Good
TEST
TEST
TEST
Mask
TEST
Good
Good
Good
Bad
Good
Block4
Bad
Good
Good
Bad
Good
Mask
TEST
TEST
Mask
TEST
Block0
Block1
Block2
Block3
Block4(Bad)
BlockN
…
DUT1
Block0
Block1
Block2
Block3
BlockN
…
DUT1
Block4 Masked
Once stored Fail Block into BBM,
the block will be masked and TTR.
Longer polling time

## Slide 113: Testing with BBM
BBM Basic Functions
  Directly write fail block data in BBM
  Counts number of fail blocks
  Generate fail block data as mask pattern
BBM Concept
  BBM captures Fail Data.
  Block based fail data of IO is compressed, and compressed fail data is called bad block information. Bad block information can control /WE or /CE pin (MASK mode)
Function Block Diagram of UBM
DR
Fail address
FC
(Format Controller)
CP
BBM
SC
(logic comparator)
MASK

## Slide 114: Comparator Mask
The Ready/Busy pin response time of bad-block could be much longer than normal-block. In order to reduce test time, BBM can mask the comparison of bad-block.
2018/6/27
tPROG = typ 200 us
tERASE = typ 2 ms
Ready/Busy pin output

## Slide 115: Driver Mask
Driver masked for Bad Block, to inhibit writing operation to prevent device goes busy state of write operation.
Good Block
Bad Block
Write Operation for Good Block
Write Operation for Bad Block

## Slide 116: Set up BBM
BbmConfigHandle can set up BBM.
BbmConfigHandle bbm_config_handle = UTL_GetBbmConfigHandle();
UTL_SetBbmConfigMode ( bbm_config_handle, UT_BBM_MAXFAIL );
UTL_SetBbmConfigAction ( bbm_config_handle, UT_BBM_CPDRINH );
UTL_SetBbmConfigWriteEnableAllDut ( bbm_config_handle, UT_ON );
UTL_SetBbmConfigAddrAssign ( bbm_config_handle, 0, UT_SIG_X( 7) );
UTL_SetBbmConfigAddrAssign ( bbm_config_handle, 1, UT_SIG_X( 8) );
UTL_SetBbmConfigAddrAssign ( bbm_config_handle, 2, UT_SIG_X( 9) );
UTL_SetBbmConfigAddrAssign ( bbm_config_handle, 3, UT_SIG_X(10) );
UTL_SetBbmConfigAddrAssign ( bbm_config_handle, 4, UT_SIG_X(11) );
UTL_SetBbmConfigAddrAssign ( bbm_config_handle, 5, UT_SIG_X(12) );
UTL_SetBbmConfigAddrAssign ( bbm_config_handle, 6, UT_SIG_X(13) );
UTL_SetBbmConfigAddrAssign ( bbm_config_handle, 7, UT_SIG_X(13) );
UTL_SetBbmConfigAddrAssign ( bbm_config_handle, 8, UT_SIG_X(14) );
UTL_SetBbmConfigAddrAssign ( bbm_config_handle, 9, UT_SIG_X(15) );
UTL_SetBbmConfigAddrAssign ( bbm_config_handle, 10, UT_SIG_X(16) );
UTL_SetBbmConfigAddrAssign ( bbm_config_handle, 11, UT_SIG_X(17) );
UTL_SetBbmConfigDataGenerationMode( bbm_config_handle, UT_BBM_MASK_SELECTEDBIT);
UTL_AddBbmConfigDrInhPin ( bbm_config_handle, 4, UT_PIN_HIGH );
UTL_SetBbmConfigCounterNoClear ( bbm_config_handle, UT_ON );
UTL_SendBbmConfig ( bbm_config_handle );
 | DISABLE | DATACAPTURE | MAXFAIL
Fail Capture | Not Available | Available | Available
DR/CP Mask with fail in BBM | Not Available | Not Available | Available
DR/CP Mask with Bad Block Count | Not Available | Not Available | Available
Set up Block-Addresses
  Select MASK PIN
Do not clear BBM
at pattern start
 | Action
MASKINH | Do not mask DR or CP
CPINH | Mask only CP
CPDRINH | Mask both of DR and CP
Enable Fail Capture

## Slide 117: Read BBM
BbmAccessHandle can read out Bad Block information from BBM.
BbmAccessHandle bbm_access_handle = UTL_GetBbmAccessHandle();
uint32_t bbm_data[ 0x1000];
dut_cursor = UTL_GetDutCursor ( UT_CDUT );
while( ( dut = UTL_NextDut( dut_cursor) ) != UT_NOMORE ) {
UTL_SetBbmAccessDut ( bbm_access_handle, dut );
UTL_ReadBbm ( bbm_access_handle, bbm_data, sizeof bbm_data);
for ( bbm_address=0; bbm_address<0x1000; bbm_address++) {
if ( bbm_data[ bbm_address] ) printf("Block %d is Bad Block\n", bbm_address);
}
}
UTL_DeleteCursor( dut_cursor );
UTL_DeleteHandle( bbm_access_handle );

## Slide 118: Read Bad Block Count
BbmAccessHandle can read out the numbe of Bad Blocks in BBM.
BbmAccessHandle bbm_access_handle = UTL_GetBbmAccessHandle();
uint32_t bbm_data[ 0x1000];
int status;
dut_cursor = UTL_GetDutCursor ( UT_CDUT );
while( ( dut = UTL_NextDut( dut_cursor) ) != UT_NOMORE ) {
UTL_SetBbmAccessDut ( bbm_access_handle, dut );
printf("DUT%d Bad Block Count:%d\n",dut,
UTL_ReadBadBlockCounter ( bbm_access_handle, &status));
}
UTL_DeleteCursor( dut_cursor );
UTL_DeleteHandle( bbm_access_handle );

## Slide 119: Write BBM
BbmAccessHandle can write Bad Block information into BBM. For example, the Bad Block information comes from previous test system. In this case, it is necessary to write Bad Block information before run test.
BbmAccessHandle bbm_access_handle = UTL_GetBbmAccessHandle();
uint32_t bbm_data[ 0x1000];
dut_cursor = UTL_GetDutCursor ( UT_CDUT );
while( ( dut = UTL_NextDut( dut_cursor) ) != UT_NOMORE ) {
... Bad Block Information into ddbm_data[] ...
UTL_SetBbmAccessDut ( bbm_access_handle, dut );
UTL_WriteBbm ( bbm_access_handle, bbm_data, sizeof bbm_data);
}
UTL_DeleteCursor( dut_cursor );
UTL_DeleteHandle( bbm_access_handle);

## Slide 120: Clear BBM
BbmAccessHandle can clear Bad Block information in BBM.
BbmAccessHandle bbm_access_handle = UTL_GetBbmAccessHandle();
UTL_PresetBbm ( bbm_access_handle, 0);
UTL_DeleteHandle( bbm_access_handle);

## Slide 121: How to use ECC

## Slide 122: Outline
ECC (Error Correction Code) is the function to correct errors in read data. Today, most memory controller for storage has ECC function. That means some errors can be acceptable for NAND FLASH.
NAND
memory
controller
MPU/MCU
001101...
001101...
001101...0100
001111...0100
ECC data
Error was found
in read-data
memory controller
corrects the error

## Slide 123: Hardware of ECC
Tester counts the number of fails in a page, and judge it’s pass or fail.
      PASS/FAIL judgement is done during pattern execution
      Store Fail Information into BBM.
ECC Counters
Limit
BBM
SC
(ALPG)
EN
CLR
JUDGE
0 0 1 1 0 0 …  0 0 1 1 1 0 …

## Slide 124: Operation to judge ECC
ECC can be control with 3 MUT signal
      Clear Counter
      Enable to count fails
      Judge PASS/FAIL
Timing chart of Read operation
Clear
ECC counter
Judge
PAS/FAIL
Enables
to count

## Slide 125: How to set up ECC function
EccConfigHandle and FailSelPinHandle can set up ECC function.
FailSelPinHandle fail_sel_pin_handle = UTL_GetFailSelPinHandle();
UTL_SetFailSelPinTarget ( fail_sel_pin_handle, UT_FAILSELPIN_TARGET_ECC_TOTAL);
UTL_SetFailSelPin ( fail_sel_pin_handle, 33, UT_ON );
:
UTL_SetFailSelPin ( fail_sel_pin_handle, 40, UT_ON );
UTL_SendFailSelPin ( fail_sel_pin_handle );
EccConfigHandle ecc_config_handle = UTL_GetEccConfigHandle();
UTL_SetEccConfigCounterLimit ( ecc_config_handle, UT_ECC_COUNTMODE_TOTAL, 1, 16);
// Set Count mode and maximum fails of PASS
// UT_ECC_COUNTMODE_TOTAL: Counts fail for each pins
// UT_ECC_COUNTMODE_OR : Counts ORed fails
UTL_SetEccConfigCounterEnableSignal( ecc_config_handle, 0, UT_SIG_C(16));
UTL_SetEccConfigJudgeSignal ( ecc_config_handle, 0, UT_SIG_C(17));
UTL_SetEccConfigCounterClearSignal ( ecc_config_handle, UT_SIG_C(18));
UTL_SendEccConfig ( ecc_config_handle );
Target pins to store

## Slide 126: How to operate in pattern
Add ECC control MUT signals.
SDEF ECC_CNT = C16
SDEF ECC_JDG = C17
SDEF ECC_CLR = C18
START READ_DATA
NOP TS1 XB<XH TP1<#00
LRD: NOP TS1 CMD YB<0 ECC_CLR ; Clear ECC Counter for each Page loop
NOP TS1 ADR1 X<XB Y<YB
NOP TS1 ADR2 X<XB Y<YB
NOP TS1 ADR3 X<XB Y<YB
NOP TS1 ADR4 X<XB Y<YB
NOP TS1 ADR5 X<XB Y<YB TP1<#30
NOP TS1 CMD
NOP TS1 NOP
NOP TS1 NOP
FLGLI1 . TS2 NOP
NOP TS1 NOP
IDXI8 . TS1 DOUT X<XB Y<YB YB<YB+1 ECC_CNT ; Enable ECC counter to count fails
NOP TS1 ECC_JDG ; Judge PASS/FAIL based on ECC counter
JNI1 LRD TS1 XB<XB+1
JNI2 LRD TS1
STPS
Timing chart of Read operation
Clear
ECC counter
Judge
PAS/FAIL
Enables
to count

## Slide 127: How to use FlashCounter

## Slide 128: Outline
Flash-Counter counts polling cycle number for each DUT. Flash-Counter can work with BBM, once over the limit, that block will be Bad Block to mask real time.
Page1(RB)
Page2(RB)
Page3(RB)
Page4(RB)
Page5(RB)
Page6(RB)
Page7(RB)
Page8(RB)
520us
550us
485us
750us
395us
635us
520us
515us
meas
Count
Result
Eg) Polling time Spec=600us
Rate = 1us, Limit=600
520
550
485
750
---
---
---
---
Pass
Pass
Pass
Fail
Masked
Masked
Masked
Masked
Spec
600us
Block 0 will be Bad block
After that it’ll be masked
real time. (Tester doesn’t have to wait longer polling time)
After masked, 1) Program/Erase , 2) Read(comparison) are masked to avoid 1) Over Proragm/Erase, 2) Wait longer polling time.

## Slide 129: Set up FlashCounter
FlashHandle can set up FlashCounter.
FlashHandle flash_handle = UTL_GetFlashHandle();
UTL_SetFlashLimitAllDut ( flash_handle, 32 );
UTL_SetFlashModeAllDut ( flash_handle, UT_FLASH_MAXFAIL );
UTL_SetFlashHoldModeAllDut ( flash_handle, UT_FLASH_MATCH2 );
UTL_SetFlashHoldConditionAllDut ( flash_handle, UT_SIG_FLAGS, UT_SIG_C(15));
UTL_SetFlashCounterConditionAllDut( flash_handle, UT_SIG_C(14), UT_SIG_C(13));
UTL_SendFlash ( flash_handle );
Start hold(ignore fails of unmatch in polling)
FLGLI = FLAGS
MAXFAIL:DR inhibit for matched DUT
or over limit
mode | function
MATCH | Match polling with R/B pin.
MATCH2 | Match polling with R/B pin. Inhibit to clear FlashCounter when FlashCounter = Limit
STACK | Match polling with Stack register to store fails for each pins.
STACK2 | Match polling with Stack register to store fails for each pins. Inhibit to clear FlashCounter when FlashCounter = Limit
Reset hold (return normal mode)
Need to reset hold status after polling
Enable FlashCounter to count polling cycles
Reset FlashCounter before polling

## Slide 130: How to operate in pattern
Add ECC control MUT signals.
SDEF FCNT_CLR = C13
SDEF FCNT_ENB = C14
SDEF HOLD_CLR = C15
START READ_DATA
NOP TS1 XB<XH TP1<#00
LRD: NOP TS1 CMD YB<0 ECC_CLR
NOP TS1 ADR1 X<XB Y<YB
NOP TS1 ADR2 X<XB Y<YB
NOP TS1 ADR3 X<XB Y<YB
NOP TS1 ADR4 X<XB Y<YB
NOP TS1 ADR5 X<XB Y<YB TP1<#30
NOP TS1 CMD
NOP TS1 NOP
NOP TS1 NOP FCNT_CLR ; Clear FlashCounter
FLGLI1 . TS2 NOP FCNT_ENB ; Count polling cycles
NOP TS1 NOP HOLD_CLR ; Reset hold state
IDXI8 . TS1 DOUT X<XB Y<YB YB<YB+1 ECC_CNT
NOP TS1 ECC_JDG
JNI1 LRD TS1 XB<XB+1
JNI2 LRD TS1
STPS
Timing chart of Read operation
Clear
Flash counter
Reset
Hold
Enables
to count

## Slide 131: How to use FCM

## Slide 132: Outline
FCM (Fail Capture Memory) is used for fail-analysis by capturing error address information.

## Slide 133: Set up FCM
FcmConfigHandle can set up FCM.
FcmConfigHandle fcm_config_handle = UTL_GetFcmConfigHandle();
UTL_AddFcmConfigPinAssign ( fcm_config_handle, 0, PIN 33 );
UTL_AddFcmConfigPinAssign ( fcm_config_handle, 1, PIN 34 );
:
UTL_AddFcmConfigPinAssign ( fcm_config_handle, 6, PIN 39 );
UTL_AddFcmConfigPinAssign ( fcm_config_handle, 7, PIN 40 );
UTL_SetFcmConfigBitSize ( fcm_config_handle, 8 IO );
UTL_SetFcmConfigAddrAssign ( fcm_config_handle, 0, UTL_SIG_Y( 0) );
UTL_SetFcmConfigAddrAssign ( fcm_config_handle, 1, UTL_SIG_Y( 1) );
:
UTL_SetFcmConfigAddrAssign ( fcm_config_handle, 12, UTL_SIG_Y(12) );
UTL_SetFcmConfigAddrAssign ( fcm_config_handle, 13, UTL_SIG_Y(13) );
UTL_SetFcmConfigAddrAssign ( fcm_config_handle, 14, UTL_SIG_X( 0) );
UTL_SetFcmConfigAddrAssign ( fcm_config_handle, 15, UTL_SIG_X( 1) );
:
UTL_SetFcmConfigAddrAssign ( fcm_config_handle, 19, UTL_SIG_X( 5) );
UTL_SetFcmConfigAddrAssign ( fcm_config_handle, 20, UTL_SIG_X( 6) );
UTL_AddFcmConfigAction ( fcm_config_handle, 1, UT_FCM_TOTALFAIL);
UTL_SetFcmConfigTransferSize( fcm_config_handle, 16384 );
UTL_SendFcmConfig ( fcm_config_handle );
  Set up FCM addresses
  Set up pins to capture
Capture all fails
transfer size from BM to FCM
(see next page)

## Slide 134: Prepare to Read/Write FCM data
FcmAccessHandle can read FCM data
FcmAccessHandle fcm_access_handle = UTL_GetFcmAccessHandle();
unsigned int fcm_data[ 0x40000];
UTL_SetFcmAccessAllBit ( fcm_access_handle, UT_OFF );
UTL_SetFcmAccessBitBlock ( fcm_access_handle, 1 );
UTL_SetFcmAccessAddrAssign( fcm_access_handle, 0, UTL_SIG_Y( 0) );
UTL_SetFcmAccessAddrAssign( fcm_access_handle, 1, UTL_SIG_Y( 1) );
:
UTL_SetFcmAccessAddrAssign( fcm_access_handle, 12, UTL_SIG_Y(12) );
UTL_SetFcmAccessAddrAssign( fcm_access_handle, 13, UTL_SIG_Y(13) );
UTL_SetFcmAccessAddrAssign( fcm_access_handle, 14, UTL_SIG_X( 0) );
UTL_SetFcmAccessAddrAssign( fcm_access_handle, 15, UTL_SIG_X( 1) );
:
UTL_SetFcmAccessAddrAssign( fcm_access_handle, 19, UTL_SIG_X( 5) );
UTL_SetFcmAccessAddrAssign( fcm_access_handle, 20, UTL_SIG_X( 6) );
UTL_SetFcmAccessApLink ( fcm_access_handle, UT_FCM_APLINK_YXZ );
UTL_SetFcmAccessXAddr ( fcm_access_handle, 0, 0x00007F );
UTL_SetFcmAccessYAddr ( fcm_access_handle, 0, 0x003FFF );
UTL_SetFcmAccessAllDut ( fcm_access_handle, UT_OFF );
DutCursor dut_cursor = UT_GetDutCursor( UT_CDUT);
while((dut = UT_NextDut( dut_cursor)) != UT_NOMORE) {
UTL_SetFcmAccessDut ( fcm_access_handle, dut );
for ( io=0; io<8; io++) {
UTL_AddFcmAccessBit ( fcm_access_handle, io );
UTL_ReadFcm ( fcm_access_handle, fcm_data, sizeof fcm_data);
}
}
UTL_DeleteCursor( dut_cursor);
FCM Access Addressing
Direction to access
Area to access
fcm_data[ 0] = 00000000000000000001110000000000
fcm_data[ 1] = 00000000000000000000000000000010
fcm_data[ 2] = 00000000000011101101110111111111
fcm_data[ 3] = 11110000000000000000000000001010
fcm_data[ 4] = 10101000000000000001010101010101
fcm_data[ 5] = 00000000000000000000000000011111
fcm_data[ 6] = 11111111111111111111111111111111
fcm_data[ 7] = 00000000000001010101010000000000
fcm_data[ 8] = 00001010101010101000000000000000
fcm_data[ 9] = 00000000000011111111111111111111
image of fcm_data and direction of addresses

## Slide 135: How to use MatchGroup

## Slide 136: Outline
ONFi device output busy flag from RB_n. But eMMC return such response from CMD or DAT0. That’s why tester have to care both. MatchGroup function help to handle it.

## Slide 137: How to set up MatchGroup
Set up MatchGroup with PinHandle and MatchPinGroupHandle.
PinHandle pin_handle_cmd = UTL_GetPinHandle();
... Other Pin setting of CMD ...
UTL_SetPinMatchMode ( pin_handle_cmd, UT_SIG_MATCHGROUP);
UTL_SetPinMatchGroup ( pin_handle_cmd, UT_MPG_SEL1 );
UTL_SendPin ( pin_handle_cmd, "CMD" );
PinHandle pin_handle_dat0 = UTL_GetPinHandle();
... Other Pin setting of CMD ...
UTL_SetPinMatchMode ( pin_handle_dat0, UT_SIG_MATCHGROUP);
UTL_SetPinMatchGroup ( pin_handle_dat0, UT_MPG_SEL2 );
UTL_SendPin ( pin_handle_dat0, "DAT0" );
MatchPinGroupHandle match_pin_group_handle = UTL_GetMatchPinGroupHandle();
UTL_SetMatchPinGroupSignal ( match_pin_group_handle, UT_MPT_SEL1, UT_SIG_C(28) );
UTL_SetMatchPinGroupSignal ( match_pin_group_handle, UT_MPT_SEL2, UT_SIG_C(29) );
UTL_SendMatchPinGroup ( match_pin_group_handle );
CMD used for
match polling with C28
DAT0 used for
match polling with C29

## Slide 138: Pattern Program
Put MUT signal for Each polling with FLGLI loop. CMD match-loop wait the header of response. DAT0 match-loop wait the busy-flag off.
SDEF CMD_MATCH = C28
SDEF DAT0_MATCH = C29
... Input WRITE_MULTIPLE_BLOCK command here ...
FLGLI1 . CYP1 TS3 CLK CMD_MATCH
... Read response for WRITE_MULTIPLE_BLOCK here ...
BLOCK_LOOP: ... Data Write here ...
FLGLI1 . CYP2 TS8 CLK CMD_W DAT0_MATCH
JNI1 BLOCK_:LOOP XB<XB+1 YB<0

## Slide 139: How to use PDS memory

## Slide 140: Outline
PDS-memory is called “Huge Cycle Palette”. This is because both functions realize PDS changing on the fly.
The background of PDS-memory development is to support serial I/F device, such as NAND flash with LPC(Low Pin Compress) and SPI.
In presentation material, PDS-memory is sometimes called “Serializer”. PDS-memory and Serializer is same function.

## Slide 141: Sample Case
This figure is the read command instruction sequence diagram of SPI-NOR device. Command instruction must be input from DI in cycle 0 - 7. Address must be input from DI in cycle 8 - 31. And Data output from DO in cycle 32 ～.
Cycle | SI(DQ0) | SO(DQ1) | 
0 | CMD:7 | - | 
: |  |  | 
7 | CMD:0 | - | 
8 | ADR:23 | - | 
: |  |  | 
31 | ADR:0 | - | 
32 | - | DAT:7 | Byte 0
: |  |  | 
39 | - | DAT:0 | 
40 | - | DAT:7 | Byte 1
: |  |  | 
47 | - | DAT:0 | 
: |  |  | 

## Slide 142: Design PDS memory
If you want SD for CMD, X for ADR and D for Data, PDS memory set up as right table.
Cycle | SI(DQ0) | SO(DQ1)
0 | SD7 | FL
: |  | 
7 | SD0 | FL
8 | X23 | FL
: |  | 
31 | X0 | FL
32 | FL | D7
: |  | 
39 | FL | D0
Reuse same PDS
for all Byte
Loop here
Port A
Port B

## Slide 143: Set up PDS-memory
PdsMemoryHandle can set up PDS-memory.
pds_memory_handle= UTL_GetPdsMemoryHandle();
UTL_SetPdsMemoryIncPat ( pds_memory_handle, UT_SIG_C(10));
UTL_SetPdsMemoryClearPat ( pds_memory_handle, UT_SIG_C(11));
UTL_SetPdsMemoryJumpPat ( pds_memory_handle, UT_SIG_C(12));
UTL_SetPdsMemoryJumpAddr ( pds_memory_handle, 32 );
UTL_SetPdsMemoryPat ( pds_memory_hadnle, 0, UT_PDS_DATAMUX_A, UT_SIG_SD( 7));
:
UTL_SetPdsMemoryPat ( pds_memory_hadnle, 7, UT_PDS_DATAMUX_A, UT_SIG_SD( 0));
UTL_SetPdsMemoryPat ( pds_memory_hadnle, 8, UT_PDS_DATAMUX_A, UT_SIG_X (23));
:
UTL_SetPdsMemoryPat ( pds_memory_hadnle, 31, UT_PDS_DATAMUX_A, UT_SIG_X ( 0));
UTL_SetPdsMemoryPat ( pds_memory_hadnle, 32, UT_PDS_DATAMUX_A, UT_SIG_FL );
:
UTL_SetPdsMemoryPat ( pds_memory_hadnle, 39, UT_PDS_DATAMUX_A, UT_SIG_FL );
UTL_SetPdsMemoryPat ( pds_memory_hadnle, 0, UT_PDS_DATAMUX_B, UT_SIG_FL );
:
UTL_SetPdsMemoryPat ( pds_memory_hadnle, 31, UT_PDS_DATAMUX_A, UT_SIG_FL );
UTL_SetPdsMemoryPat ( pds_memory_hadnle, 32, UT_PDS_DATAMUX_A, UT_SIG_D ( 7));
:
UTL_SetPdsMemoryPat ( pds_memory_hadnle, 39, UT_PDS_DATAMUX_A, UT_SIG_D ( 0));
UTL_SendPdsMemory ( pds_memory_handle );
Increament PDS-memory AP with C10
PDS-memory AP = 0 with C11
Jump PDS-memory AP with C12
Jump address of PDS-memory AP
DataMux A
DataMux B

## Slide 144: Pin setting for PDS-memory
PdsMemorySelHandle can set up the relationship between PDS-memory Port and Pin.
PdsMemorySelHandle pds_memory_sel_handle;
pds_memory_sel_handle = UTL_GetPdsMemorySelHandle();
UTL_SetPdsMemorySelPinList( pds_memory_sel_handle, "DI" );
UTL_SetPdsMemorySelDataMux( pds_memory_sel_handle, UT_PORT_A, UT_PDS_DATAMUX_A);
UTL_ClearPdsMemorySelDut ( pds_memory_sel_handle );
UTL_SendPdsMemorySel ( pds_memory_sel_handle );
UTL_DeleteHandle ( pds_memory_sel_handle );
pds_memory_sel_handle = UTL_GetPdsMemorySelHandle();
UTL_SetPdsMemorySelPinList( pds_memory_sel_handle, "DO" );
UTL_SetPdsMemorySelDataMux( pds_memory_sel_handle, UT_PORT_A, UT_PDS_DATAMUX_B);
UTL_ClearPdsMemorySelDut ( pds_memory_sel_handle );
UTL_SendPdsMemorySel ( pds_memory_sel_handle );
SI=Port A
SO=Port B

## Slide 145: Pattern for PDS-memory
To use PDS-memory, Put MUT to clear PDS-memory AP, increase and jump
SDEF SER_INC = C10 ; Increament PDS-Memory-Pointer(Serializer = PDS-Memory)
SDEF SER_CLR = C11 ; Clear PDS-Memory-Pointer (Serializer = PDS-Memory)
SDEF SER_JMP = C12 ; Jump PDS-Memory-Pointer (Serializer = PDS-Memory)
:
START #0000
NOP XB<0 YB<0 TP1<TPH1 TP2<#003 ;
LRD00: NOP CS SER_CLR ;
IDXI8 30 CS SCLK W SER_INC ;CMD:8 + ADR:24
LDR01: NOP CS SCLK R SER_INC YB<YB+1 ;DAT 7
NOP CS SCLK R SER_INC YB<YB+1 ;DAT 6
NOP CS SCLK R SER_INC YB<YB+1 ;DAT 5
NOP CS SCLK R SER_INC YB<YB+1 ;DAT 4
NOP CS SCLK R SER_INC YB<YB+1 ;DAT 3
NOP CS SCLK R SER_INC YB<YB+1 ;DAT 2
NOP CS SCLK R SER_INC YB<YB+1 ;DAT 1
JNI2 LRD01 CS SCLK R SER_JMP XB<XB+1 YB<0 ;DAT 0
NOP CS ;
NOP ;
JNI3 LRD00 ; Page loop
JNI4 LRD00 ; Sector loop
JNI5 LRD00 ; Block loop
NOP ;
STPS
Loop for data-output
all bytes
Loop for
command/address input