## Slide 1: 珠海创飞芯科技有限公司 2018 April Monthly Review
2018年5月2日

## Slide 2
创飞芯2018-2019未来两年产品开发计划
    2018/5/1 3.3v and 1.8v 16Mb 65nm SPI NOR foundry nto (Done)
    2018/7/1 3.3v and 1.8v 4Mb and 3.3v 16Mb 65nm SPI NOR 1st Si
      2018 2nd half 1.8v 4Mb and 3.3v 16Mb SPI NOR量产
    2018/10/1 3.3v and 1.8v 256Mb 65nm SPI NOR nto (Design on-going)
      2019 Q2 128Mb/256Mb SPI NOR量产
    2018/10/1 2Gb 24nm SLC NAND foundry nto (Design on-going)
      April 2018, NAND design kick off at full speed execution phase (Done)
    2018/12/31 2Gb 24nm NAND 1st Si
      2019 Q2 24nm NAND risk production
    2019/10/1 24nm MLC NAND nto
      2019/12/31 24nm MLC NAND 1st Si
    2018 3.3v PROM Cast-C 可靠认证 (Qual on-going)
      兰州qual is OK. 北大qual this week
    OTP: 11LL Silterra OTP test chip tapeout before 2018/5/7 this weekend
      22nm at GF, 130nm at SMIC and etc

## Slide 3: 2018-2019 ElderSens Product Launch Plan
    2018/5/1 Reusable Smart Diaper Sensor Amazon Launch
      Phase 1: DiaperSens adhesive refill Amazon listed
      Phase 2: DiaperSens Sensor Amazon to be listed in May
    2018/10/1 ElderSens Edge Computing Router Amazon Launch
    2018/11/11 Disposable Smart Diaper Amazon Launch
    2019/4/1 ElderSens Geo-Fencing System Amazon Launch
    2019/10/1 ElderSens VitalSens Amazon Launch

## Slide 4: NAND 24nm 2Gb SLC
Verify the design material/environment
  PDK from SMIC : need to modify DRC inhouse
  Server environment for design and simulation
  Document and communication : google drive, zoom
Set design target spec
  Exact column/block/plane number : 2200byte/1048 block/2plane
  Compatible design reference die : Micron 2Gb SLC ONFI 1.0 spec
  Pin layout and supply voltage : ONFI 1.0 1.8v for now, add 3v later
  Internal test sequence
Status : Top-down
  Use Verilog to quick model chip behavior and internal RTL FSM, some simple operate without array is ok
  Memory operation sequence
Status : Bottom-up
  Verify PDK design rule
    Memory array : have schematic, but layout LVS/DRC ongoing
    Sense Amp and page buffer, concept document ready, need to simulation 1 bit SA first
    Block decoder and WL driver : need to work on it soon
  STD cells
    Still need to provide schematic and Verilog reference
  Leaf modules
    BGR 80% done, just add NMOS voltage for current reference output
    HV pump need to swap HVNMOS to HVPMOS as lacking triple well device

## Slide 5: ElderSens April Monthly Review, May Monthly Plan
    2018/5/1 Reusable Smart Diaper Sensor Amazon Launch
      Phase 1: DiaperSens adhesive refill Amazon listed
      Phase 2: DiaperSens Sensor Amazon to be listed in May (IOS, Android Apps and firmware saved in Bitbuckit and Google Drive. PCB, FPC, BOM, and industry designs saved in Google Drive.)
      DiaperSens market campaign with Business Wire, Amazon, Google… after Amazon listing
    2018/5/1 DiaperSens go to market readiness and launch
      Deployed and completed system installation and acceptance in SanEi (Japan) and Suntime (Hong Kong)
    2018/11/1 ElderSens edge computing Router launch
      Initiated discussion for product definition

## Slide 6: NOR FLASH
Tasks Completed By the End of 04/30
Design and Implemented 1.8V Norflash conversion circuits
  Plan developed to convert existing 3.3V Norflash to 1.8V
  Power conversion modules designed, simulated and full chip integration.
  Full chip power control simulated and limited full chip function simulated
  Full chip erase problem found and solved, with verification
Norflash GDS frontend tapeout of 10 splits
  6 splits of Norflash 16Mbits 3.3v design
  4 splits of Norflash 4Mbits 1.8v design
Norflash production test flow preparation
Future Tasks
Norflash production test
  Complete production test plan documentation
  Finish production test drill and practice
Norflash GDS backend tapeout targeted 05/28
  Layout improvement on metal routing
  Supplementary design verifications on both functionality and corners
New Norflash Design Kick off
  1.8v /3.3v SPI Norflash 256/128Mbits
    Native 1.8v VDD Design
    Possible brand new or improved controlling architecture
    Possible expanded command sets

## Slide 7: Android APP & Google & Youtube
1.Fireware encrypt，CRC ，rolling counter
2.Android app decrypt，CRC，rolling counter
3.Can browse Google and youtube.
4.Diapersens IOS app update.
5.Esprotal ANDROID app test success.
6.Japan & HongKong customer has been used Esprotal ios app.